## Slide 1
Location-Constrained Fits

## Slide 2
Location-Constrained Fits
Identify the fit features
Identify the contact surfaces
Determine the contact surface priority

## Slide 3
3 Contact Surfaces
2 Fit features

## Slide 4
Fit Features
1st fit feature
2nd fit feature
The 1st or primary fit feature is usually the one with the tighter fit. However, any order is acceptable
Notes: Unlike the contact surfaces, the order in which fit features are specified does not make a difference – Any order is acceptable. However, it is common to specify the fit features with tighter fits first.

## Slide 5
Contact Surfaces
Contact features are planar surfaces which are required to make closest contact for the fit to be acceptable
A fit can have up to 3 fit-related contact surfaces.
Contact surfaces have order or priority in a fit

## Slide 6
Contact Surfaces
Contact surface
Contact surface
Contact surface

## Slide 7
Contact surfaces are planar surfaces which are required to make closest contact for the fit to be acceptable
Contact Surfaces
Primary Contact Surface (PCS) makes the fullest contact subject to no constraints
Secondary Contact Surface (SCS) makes the 2nd fullest contact subject to PCS constraint
Tertiary Contact Surface (TCS) makes the 3rd fullest contact subject to PCS and SCS constraints

## Slide 8
The design dictates the contact surface priority
Contact Surfaces
Primary contact surface is usually obvious and easy to identify. Surfaces pushed together by fasteners are the most common
Unless the design dictates, the choice of the secondary and tertiary contact surfaces is made arbitrarily. The convention is to use the larger surface as the secondary.

## Slide 9
Priority of Contact Surfaces
Primary Contact Surface
Secondary Contact Surface
Tertiary Contact Surface

## Slide 10
Dialog window for selecting the Primary Contact Surface (PCS)

## Slide 11
Contact Surfaces
PCS
SCS
TCS

## Slide 12
Result after selecting the primary contact surface

## Slide 13
Dialog window for selecting the Secondary Contact Surface (SCS)

## Slide 14
Result after selecting the secondary contact surface

## Slide 15
Dialog window for selecting the Tertiary Contact Surface (TCS)

## Slide 16
Result after selecting the Tertiary Contact Surface

## Slide 17
Fit Features
Primary fit Feature (PFF)
Secondary Fit Feature (SFF)

## Slide 18
Dialog window for selecting the Primary Fit Feature (PFF)
Notes: This is the dialog window for the first or the primary fit feature. The fit feature is a pattern of two bosses. The bottom part of the Feature Type selection is for fastener fit features which will be covered later.

## Slide 19
Result after selecting the primary fit feature

## Slide 20
Dialog window after PFF selection and pressing ESC
What about the Secondary Fit Feature?
Notes: After selecting the three contact surfaces along with the primary fit feature the program indicates that the task is finished. This might be puzzling because we have not done the second pattern of fit features yet. This will be explained shortly.

## Slide 21
Final dialog window after pressing OK

## Slide 22
Obviously the fit is not finished – the smaller bosses have not been toleranced for fit.
This is because the total number of fit features and contact surfaces in any tolerance statement must be 4 or less. In this example we have 5 total CS and FF
PFF
PCS
SCS
TCS

## Slide 23
We need to run the program only once if we have:
  3 CS + 1 FF
  2 CS and 2 or less FF
  1 CS and 3 or less FF
  0 CS and 4 or less FF
If there are more FF run the program again for each additional FF

## Slide 24
If there are more fit features, run the program again once for every additional fit feature
New FF
PCS
SCS
TCS
Exactly the same contact features as in the first statement
Notes: Since we have 3 contact surfaces and 2 fit features we must run the program again selecting exactly the same three contact surfaces but this time with the new pattern of fit features.

## Slide 25
Continue with the fit of the pattern of smaller bosses by running the program again.
Since PCS is already selected there is no need to reselect it

## Slide 26
Since SCS is already selected there is no need to reselect it

## Slide 27
Since TCS is already selected there is no need to reselect it

## Slide 28
Select the new FF in the dialog window for the PFF

## Slide 29
The part is now fully toleranced for fit

## Slide 30
See the fit analysis which is usually done after both parts are toleranced

## Slide 33
Apply the same procedure to the mating part with holes

## Slide 34
Result after selecting the primary contact surface

## Slide 35
Result after selecting the secondary contact surface

## Slide 36
Result after selecting the Tertiary Contact Surface

## Slide 37
Result after selecting the primary fit feature

## Slide 40
The part is now fully toleranced for fit

## Slide 41
Video Demo: Case of 3 contact surfaces and two fit features

## Slide 42: Another Example
Location-Constrained Fit
1 Contact Surface
3 Fit features
  Center hole/boss
  Slot and rail
  Pattern of holes/bosses
Fit analysis for the primary fit feature

## Slide 43
PCS
PFF
SFF
TFF

## Slide 44
Result after PCS selection

## Slide 45
Result after PFF selection
Note: A,B, and C labels are used for contact surfaces.

## Slide 46
Result after SFF selection

## Slide 47
Result after TFF selection

## Slide 48
Finished

## Slide 49
Finished tolerances for the part with pins

## Slide 50
Fit analysis for the primary fit feature

## Slide 51
Demo for the part with holes

## Slide 52
Version-1
Version-2

## Slide 53
Demo for the part with Pins

## Slide 54
Location-Constrained Fit
1 Contact Surface
2 Fit features
  Smaller hole/boss
  Larger hole/boss
Set up tolerances to assure fit while contact surfaces make full contact
Example

## Slide 55
PCS
PFF
SFF

## Slide 56
Result

## Slide 57
PCS
SFF
PFF

## Slide 58
Result