## Slide 1: MCECS Guide Robot Project
Project Update
5/23/2012

## Slide 2: Agenda
Goal
Progress Report
  System Diagram
  Base (Omar Mohsin, Ali Alnasser)
  Body (David Gaskin)
  Head/Neck (Stephen Huerta)
  Arm (James )
  Vision (Danny Voils, Mathias Sunardi)
  Natural Language Processing (Robert Fiszer)
To Do List

## Slide 3: Goal
Demo towards the end of Spring Term 2012:
  Base, body, and head assembled.
  Robot can move around the Engineering Building atrium autonomously or by remote.
  Robot can avoid obstacles and/or collision with obstacles.
  Robot can display simple gestures.
  Few simple interactions.

## Slide 4: System Diagram
Kinect
(Vision)
Router
PC
Tablet/Head
(UI)
Neck
ArduinoMEGA
Microcontroller
Body
+
Base
Sensors On Base
Motor Controllers
Rotary Encoders
DC Motors
(Wheels)
Linear Actuators
(Waist)
Limit Switch
(Bumpers)
Sonar
(Proximity)

## Slide 5: Base

## Slide 6: Base
Omar Mohsin, Ali Alnasser
Avoids obstacles
Navigate safely
Storage:
  Battery
  PC
  Base & body motor controllers
Bumpers to detect collisions
ArduinoMEGA
Microcontroller
PC
Rotary Encoders
DC Motors
(Wheels)
Limit Switch
(Bumpers)
Sonar
(Proximity)

## Slide 7: Base
Progress/Current State:
  Encoders, batteries, battery charger, power management board, limit switches have been purchased.
  Battery selected for ~2 hours (normal operation).
  Testing to determine best proximity/obstacle avoidance policy.
  Waiting for motor controllers.
Rotary Encoders
DC Motors
(Wheels)
Limit Switch
(Bumpers)
Sonar
(Proximity)
ArduinoMEGA
Microcontroller
PC

## Slide 8: Base
Controllers
  PC
  ArduinoMEGA
  Motor Controller
Sensors:
  Limit Switch (x8)
  Sonar (x12)
  Rotary Encoders (x4)
Actuators:
  DC Geared Motor (x4)
ArduinoMEGA
Microcontroller
PC
Rotary Encoders
DC Motors
(Wheels)
Limit Switch
(Bumpers)
Sonar
(Proximity)

## Slide 9: Base
Motor Controller:
  Controls wheels
  Rotary Encoders
  Closed-loop PID controller
Obstacle detection:
  Limit Switch for bumpers (emergency stop on collision).
  Sonar for obstacle detection & avoidance (15cm - ~6m range).

## Slide 10: Body
David Gaskin
4 Degrees of Freedom for expressive body gestures, dance motion, etc.
  Tilt
  Rotation
Base for:
  Head
  Arms
  Kinect
  User Interface (tablet, buttons, lights, speakers)
ArduinoMEGA
Microcontroller
PC
Linear Actuators
(Waist)

## Slide 11: Body
Progress/Current State:
  Calculations on range of motion.
  Working on determining top joint design.
  Programming position control.

## Slide 12: Body
Controllers:
  ArduinoMEGA
  Sabretooth motor driver
Sensors:
  Encoder (built-in in actuators)
Actuators:
  Linear Actuators (x4)
  Stepper motor (x1) (not implemented yet)
ArduinoMEGA
Microcontroller
PC
Linear Actuators
(Waist)

## Slide 13: Head/Neck
Stephen Huerta
Neck:
  2 Degrees of freedom: tilt and pan.
Head:
  Cartoon face on tablet device.
  User Interaction.
  Display responses.
PC

## Slide 14: Head/Neck
Progress/Current State:
  Early testing for motor controls.
  Research into tablet holder.
  Research into tablet programming (iOS).

## Slide 15: Head/Neck
Controllers:
  Arbotix
Actuators:
  Bioloid servos (x2)

## Slide 16: Head/User Interface (concept)
Microphone/Camera inputs (possibility)
Gives users text and visual feedback
Manual input feedback for users

## Slide 17: Head/User Interface (concept)
Microphone/Camera inputs (possibility)
Gives users text and visual feedback
Manual input feedback for users

## Slide 18: Arm
(James’ part)
PC

## Slide 19: Vision
Mathias Sunardi, Danny Voils
Object detection/recognition
Face detection/recognition
Navigation/localization
Kinect
(Vision)
PC

## Slide 20: Vision
State:
  Mathias Sunardi is working with Danny Voils to use images from Kinect for object recognition based on Danny’s thesis work.
  Mathias Sunardi is working on hallway-vanishing-point detection for navigation.
Kinect
(Vision)
PC

## Slide 21: Natural Language Processing
Status:
  No update.

## Slide 22: Navigation
Status:
  No update.

## Slide 23: To Do
Assemble sensors on base and test.
Determine safety policies for:
  Navigation (avoid collision, stairs, walls)
  Components (avoid damages to actuators, power system, controllers)
Assemble base with upper body
Construct upper body for base of neck and arm.
Design/programming User Interface
Mapping/navigation program
Main program to integrate all components

## Slide 24: Questions?

## Slide 25: Extra Slides …

## Slide 26: Head/Neck

## Slide 27: Head/Neck