## Slide 1: Intro to Movement of robots and introduction to kinematics of robots
Notes: January 21, 2002

## Slide 2
Kinematics: constraints on getting around the environment
The effect of a robot’s geometry on its motion.
kinematics
from sort of simple to sort of difficult
manipulator modeling
wheeled platforms

## Slide 3: Effectors and Actuators
An effector is any device that affects the environment.
A robot's effector is under the control of the robot.
Effectors:
  legs,
  wheels,
  arms,
  fingers.
The role of the controller is to get the effectors to produce the desired effect on the environment,
  this is based on the robot's task.

## Slide 4: Effectors and Actuators
An actuator is the actual mechanism that enables the effector to execute an action.
Actuators typically include:
  electric motors,
  hydraulic cylinders,
  pneumatic cylinders,
  etc.
The terms effector and actuator are often used interchangeably to mean "whatever makes the robot take an action."
This is not really proper use:
  Actuators and effectors are not the same thing.
  And we'll try to be more precise.

## Slide 5: Kinematics for Animals (and humans)

## Slide 6: Review: degrees of freedom
Most simple actuators control a single degree of freedom,
    i.e., a single motion (e.g., up-down, left-right, in-out, etc.).
  A motor shaft controls one rotational degree of freedom, for example.
  A sliding part on a plotter controls one translational degree of freedom.
How many degrees of freedom (DOF) a robot has is very important in determining how it can affect its world,
  and therefore how well, if at all, it can accomplish its task.
We said many times before that sensors must be matched to the robot's task.
Similarly, effectors must be well matched to the robot's task also.
When you design a robot your first task is decide the number of DOF and the geometry.

## Slide 7: DOF
In general, a free body in space as 6 DOF:
  three for translation (x,y,z),
  three for orientation/rotation (roll, pitch, and yaw).
You need to know, for a given effector (and actuator/s):
  how many DOF are available to the robot,
  how many total DOF any given robot has.
If there is an actuator for every DOF, then all of the DOF are controllable.
Usually not all DOF are controllable, which makes robot control harder.
To demonstrate, use a pen in your hand…..

## Slide 8: DOF and controllable DOFs
A car has 3 DOF:
  position (x,y) and
  orientation (theta).
But only 2 DOF are controllable:
  driving: through the gas pedal and the forward-reverse gear;
  steering: through the steering wheel.
Since there are more DOF than are controllable, there are motions that cannot be done.
Example of such motions is moving sideways (that's why parallel parking is hard).

## Slide 9: DOF for animals

## Slide 10: One Minute Test
How many degrees of freedom does your hand have, with your forearm fixed in position?
(Hint: It’s not 6)
Answer on next slide

## Slide 11: Degrees of Freedom in Hand
Total
Thumb
Fingers
Palm
Wrist
Part
23
2 @ base (attached to wrist)
2 @ visible joints
4
2 @ base (Up-down & side-to-side)
1 @ each of two joints
4*4
Open-close a little
1
Side-to-side
Up-down
2
Comment
DoF
Hand has 23 degrees of freedom

## Slide 12
We need to make a distinction between what an actuator does (e.g., pushing the gas pedal) and what the robot does as a result (moving forward).
A car can get to any 2D position but it may have to follow a very complicated trajectory.
Parallel parking requires a discontinuous trajectory with respect to the velocity.
It means that the car has to stop and go.
Total and Controllable DOFs
Kinematics: wheeled platforms vs. robot arms (or legs)
VR
VL
y
x

## Slide 13
What is a HOLONOMIC robot?

## Slide 14
When the number of controllable DOF is equal to the total number of DOF on a robot, the robot is called holonomic. (i.e. the hand built by Uland Wong).
Definition of a HOLONOMIC robot
Holonomic <= > Controllable DOF = total DOF

## Slide 15
If the number of controllable DOF is smaller than total DOF, the robot is non-holonomic.
If the number of controllable DOF is larger than the total DOF, the robot is redundant. (like a human hand, we did not build such robot yet)
DOF versus types of robots
Non-Holonomic <= > Controllable DOF < total DOF
Redundant <= > Controllable DOF > total DOF

## Slide 16: DOF for animals
A human arm has 7 DOF:
  3 in the shoulder,
  1 in the elbow,
  3 in the wrist
All of which can be controlled.
A free object in 3D space (e.g., the hand, the finger tip) can have at most 6 DOF!
So there are redundant ways of putting the hand at a particular position in 3D space.
This is the core of why robot manipulation is very hard!
One minute test!

## Slide 17: JAPAN HONDA AND SONY ROBOTS
Pino, a 70-centimeter (2-foot)-tall and 4.5-kilogram (9-pound) humanoid robot designed by Japan Science and Technology Corporation in Tokyo which can walk on its legs and respond to stimulation through a sensor, shakes hand with Malaysia's Prime Minister Mahathir Mohamad during the opening of the Expo Science & Technology 2001 in Kuala Lumpur, Malaysia, Monday, July 2, 2001. (AP Photo/Andy Wong)
Question: how many DOF?

## Slide 18: 98 degrees (of freedom)
This is in any case simplified

## Slide 19: Anatomical Coordinates and Robots that mimick animals

## Slide 20: Human Anatomical Coordinates – important in work on humanoid robots
Sagittal Plane
Coronal Plane
Transverse Plane

## Slide 21: Animal Anatomical Coordinates
We built robot fishes, horses, dogs and other animals.

## Slide 24: Prosthetic Arms and Hands

## Slide 25: Knowledge of bio-mechanics is useful to design hands, necks, heads for animatronic robots

## Slide 26: Types of kinematic Systems

## Slide 27: Robot Arms for Space, All kinds of manipulators

## Slide 28: Robot Arms for Space

## Slide 29: Serial Robotic Manipulators

## Slide 30: Serial Robotic Manipulators
Serial chain of robotic links and joints.
  Large workspace
  Low stiffness
  Cumulative errors from link to link
Proximal Link – closer to the base
Distal Link – farther from the base
Proximal links carry the weight and load of distal links
Actuation of proximal joints affects distal links.
Limited load-carrying capability at the end effector.

## Slide 34: Parallel Robotic Mechanisms

## Slide 35: Parallel Robotic Mechanisms
End plate is directly actuated by multiple links and joints.
Multiple links and joints are called a kinematic chain.
The workspace is restricted
Common link-joint configuration
This can serve as Pick-and-Place Robot
Light construction
Stiffness
High load-carrying capacity.
We use it for waist in MCECS BOT.

## Slide 36: Manipulation

## Slide 37: Manipulation

## Slide 38: Manipulation
In locomotion (mobile robot), the body of the robot is moved to get to a particular position and orientation.
In contrast - a manipulator moves itself
  typically to get the end effector (e.g., the hand, the finger, the fingertip)
  to the desired 3D position and orientation.
So imagine having to touch a specific point in 3D space with the tip of your index finger;
  that's what a typical manipulator has to do.

## Slide 39: Issues in Manipulation
In addition: manipulators need to:
  grasp objects,
  move objects.
  But those tasks are extensions of the basic reaching discussed above.
The challenge is to get there efficiently and safely.
Because the end effector is attached to the whole arm, we have to worry about the whole arm:
  the arm must move so that it does not try to violate its own joint limits,
  it must not hit itself or the rest of the robot, or any other obstacles in the environment.

## Slide 40: Manipulation - Teleoperation
Thus, doing autonomous manipulation is very challenging.
Manipulation was first used in tele-operation, where human operators would move artificial arms to handle hazardous materials.
Complicated duplicates of human arms, with 7 DOF were built.
It turned out that it was quite difficult for human operators to learn how to tele-operate such arms

## Slide 41: Manipulation and Teleoperation: Human Interface
One alternative today is to put the human arm into an exo-skeleton, in order to make the control more direct.
Using joy-sticks, for example, is much harder for high DOF.
Exoskeletons better than joysticks
Exo-skeletons used in “Hollywood Robotics”

## Slide 42: Why is using joysticks so hard?
Because even as we saw with locomotion, there is typically no direct and obvious link between:
  what the effector needs to do in physical space
  and what the actuator does to move it.
In general, the correspondence between actuator motion and the resulting effector motion is called kinematics.
In order to control a manipulator, we have to know its kinematics:
  1. what is attached to what,
  2. how many joints there are,
  3. how many DOF for each joint,
  etc.

## Slide 43: Basic Problems for Manipulation
Kinematics
  Given all the joint angles - where is the tip ?
Inverse Kinematics
  Given a tip position - what are the possible joint angles ?
Dynamics
  To accelerate the tip by a given amount how much torque should a particular joint motor put out ?

## Slide 44: Kinematics versus Inverse Kinematics
We can formalize all of this mathematically.
  To get an equation which will tell us how to convert from, say, angles in each of the joints, to the Cartesian positions of the end effector/point is called:
    computing the manipulator kinematics
  The process of converting the Cartesian (x,y,z) position into a set of joint angles for the arm (thetas) is called:
    inverse kinematics.
Something for lovers of math and programming! Publishable! LISP

## Slide 45: Manipulators

## Slide 46: Manipulators
Robot arms, industrial robot
  Rigid bodies (links) connected by joints
  Joints: revolute or prismatic
  Drive: electric or hydraulic
  End-effector (tool) mounted on a flange or plate secured to the wrist joint of robot

## Slide 47: Manipulators: Robot Configurations
Cartesian: PPP
Cylindrical: RPP
Spherical: RRP
SCARA: RRP
(Selective Compliance Assembly Robot Arm)
Articulated: RRR
Hand coordinate:
n: normal vector; s: sliding vector;
a: approach vector, normal to the
tool mounting plate

## Slide 48: Manipulators: Motion Control Methods
  Point to point control
    a sequence of discrete points
    spot welding, pick-and-place, loading & unloading
  Continuous path control
    follow a prescribed path, controlled-path motion
    Spray painting, Arc welding, Gluing

## Slide 49: Manipulators: Robot Specifications
  Number of Axes
    Major axes, (1-3) => Position the wrist
    Minor axes, (4-6) => Orient the tool
    Redundant, (7-n) => reaching around obstacles, avoiding undesirable configuration
  Degree of Freedom (DOF)
  Workspace
  Payload (load capacity)
  Precision v.s. Repeatability
Which one is more important?
Notes: Precision (validity) is defined as how accurately a specified point can be reached. It is a function of the resolution of the actuators, as well as its feedback devices. Most industrial robots can have precision of 0.001 inch or better.
Repeatability (variability) is how accurately the same position can be reached if the motion is repeated many times. The robot may not reach the same point every time, but will be within a certain radius from the desired point. The radius of a circle that is formed by this repeated motion is called repeatability. It is much more important than precision. If a robot is not precise, it will generally show a consistent error, which can be predicted and thus corrected through programming. However, if the error is random, it cannot be predicted and thus cannot be eliminated. Repeatability defines the extent of this random error. Manufactures must specify repeatability in conjunction with the number of tests, the applied payload during the tests, and the orientation of the arm. Have repeatability in the 0.001 inch range.
Depending on their configuration and the size of their links and wrist joints, robots can reach a collection of points called a workspace.
Payload is the weight a robot can carry and still remain within its other specification.

## Slide 50: Joints.
Joints connect parts of manipulators.
The most common joint types are:
  revolute link (rotation around a fixed axis)
  prismatic link (linear movement)
These joints provide the DOF for an effector.
Prismatic Link

## Slide 51: Joints.
Revolute Link

## Slide 52: Revolute Robotic Joints

## Slide 54: Prismatic Robotic Joints

## Slide 56: Other Robotic Joints

## Slide 58: Assembly Robot Configurations and Workspaces

## Slide 61: Terms for manipulation
Links and joints
End effector, tool
Accuracy vs. Repeatability
Workspace
Reachability
Manipulability
Redundancy
Configuration Space

## Slide 62
Types of Manipulators
Basic distinction: what kinds of joints extend from base to end.
“RR” or “2R”
“PR” arm
All manipulators can be represented as chains of P (prismatic) and R (rotational) joints.

## Slide 63
Prismatic Joints
Ambler
Ninja
tomato harvester

## Slide 64
Challenges in kinematics design
1. Modeling many degrees of freedom
2. No closed-form solution guaranteed for the inverse kinematics.
3. Trajectory generation under nonholonomic constraints
4. Navigating with obstacles
goal
obstacle

## Slide 65
Multiple solutions (or no solutions) for a task.
Challenges: multiple solutions

## Slide 66
Multiple solutions (or no solutions) for a task.
Challenges

## Slide 67
Opportunities
Direct kinematic/ inverse kinematic modeling - is the basis for control of the vast majority of industrial robots.
Accurate (inverse) kinematic models are required in order to create believable character animations
how would these things bike?

## Slide 68: Homogeneous Transformation

## Slide 70: Homogeneous Transformation

## Slide 73: Examples of Manipulators

## Slide 79: Manipulator Redundancy and Degeneracy

## Slide 88: Sources
Robert Stengel
Prof. Maja Mataric
Dr. Fred Martin
Bryce Tucker and former PSU students
A. Ferworn,
Prof. Gaurav Sukhatme, USC Robotics Research Laboratory
Paul Hannah
Reuven Granot, Technion
Dodds, Harvey Mudd College