## Slide 1: Mechanical Issues
Your robot can be inexpensive

## Slide 2
Agenda
  Inexpensive robot for high schools
  Raw Materials
  Other Materials
  Fasteners
  Tools
  Safety & Maintenance
Mechanical issues
  Motors
  Techniques
  Design Principles
  Other resources

## Slide 3: Your tasks
Go to Home Depot
Go to Goodwill
Go to Army Surplus stores
Go to Tektronix Country Store etc
Find rotating components of all kinds
Find linear actuation components of all kinds
Is it good for a head? Is it good for a leg?
Use of lamps – see in lab.

## Slide 4: Goal:
Be able to build a
simple robot with the tools
and materials provided in
the lab or purchased in Goodwill or Home Depot stores

## Slide 5: Raw Materials

## Slide 6: Raw Materials
Pegboard
Hardboard
Baltic Birch Plywood
Sheet Aluminum
Polycarbonate
Prototyping Foam

## Slide 7: Raw Materials: Pegboards

## Slide 8
Raw Materials:
Hardboards

## Slide 9: Raw Materials: Baltic Birch Plywood

## Slide 10: Raw Materials: Sheet Aluminum

## Slide 11: Raw Materials
Polycarbonate (1/8”, 1/4”)
  Looks really cool
  Not too hard to machine, unless it gets hot and softens
  1/8” can be sheared and hand punched
  1/4” can be cut using scroll saw and drilled
  Good for mounting gears

## Slide 12: Raw Materials
  Prototyping foam (2” blue foam)
  Large sheets available
  Good for bulky parts
  Cuts easily with hot knife
  Also can be sculpted with hot knife for interesting / irregular shapes

## Slide 13: Other materials
  Wooden dowels
  Hollow metal tubing
  Springs
  PVC pipe
  Foam pipe insulation
  Gears
  Others…

## Slide 14: Fasteners

## Slide 15: Fasteners

## Slide 16: Fasteners

## Slide 17: Fasteners
Use washers!

## Slide 18: Fasteners
  Wood glue – best with wood screws for permanent joints.
    Make a solid piece out of multiple pieces
    When glue dries, stronger than the wood around it. Dry time is long, though
  Superglue – quick and dirty, or use with other fasteners for permanence

## Slide 19
Fasteners
  If you’re not sure how well a joint will work, use scrap and test it
  Testing mechanical parts is a good idea in general, just like software
  Design for assembly and re-assembly

## Slide 20
Tools

## Slide 21
Tools
  Scroll Saw
    Thin (1/4”) wood and polycarbonate only
    Makes curved cuts
    Don’t force the blade in any direction, medium pressure will cut
    No metal allowed!

## Slide 22: Tools

## Slide 23: Tools
We used Mitre Saw for cutting thick aluminum for MCECSBOT

## Slide 24: TOOLS: Shear/ Brake
We built complete robots and necks of lions with them

## Slide 25: TOOLS: punch

## Slide 26: Safety

## Slide 27: Safety

## Slide 28: Maintenance of the Laboratory

## Slide 29: Design Techniques for robot bodies

## Slide 30: Design Techniques for robot bodies

## Slide 31: Simple Rotating Gripper

## Slide 32: Use of hydraulics/pneumatics and wood
syringes

## Slide 33: Mounting small components such as IR and Servos

## Slide 34: Techniques for Metal bending

## Slide 35: Saint Venant’s Principe for Shaft Design

## Slide 36: Example of a good mechanical design of a peg placing system

## Slide 38: Sources
Aaron Sokoloski