## Slide 1: Currents Through Parallel Resistors
470W
220W
Gnd
5V
living with the lab
© 2011 LWTL faculty team

## Slide 2
Select Resistors
Find the 220W and the 470W resistors from your parts kit.
Now, find the 220W resistor.
Example: 470W resistor
4 = yellow
7 = violet
Add 1 zero to 47 to make 470, so 1 = brown
So, 470 = yellow, violet, brown
color | digit
black | 0
brown | 1
red | 2
orange | 3
yellow | 4
green | 5
blue | 6
violet | 7
gray | 8
white | 9
first
digit
second digit
number
of zeros
tolerance
gold = ±5%
silver = ±20%
living with the lab

## Slide 3
build the parallel circuit below
measure the total current from the power source
Compute the current after you make your measurement.
current flow
current flow
living with the lab
use Ohm’s law:
compare

## Slide 4
Compute the current after you make your measurement.
current flow
living with the lab
modify the parallel circuit as show
measure the total current through the 220Ω resistor
use Ohm’s law:
compare

## Slide 5
Compute the current after you make your measurement.
living with the lab
modify the parallel circuit as show
measure the current through the 470Ω resistor
compare
use Ohm’s law:

## Slide 6
~
~
I = 22.7 mA
I = 10.7 mA
more current goes through smaller resistor
I = 33 mA
living with the lab
check for conservation of charge
Kirchoff’s Current Law (KCL) The algebraic sum of currents entering a node is zero.
Current In = Current Out