## Slide 1: Analog and Digital Measurements
living with the lab
14 digital input / output pins
6 analog input pins
© 2011 LWTL faculty team

## Slide 2
living with the lab
A digital system is a data technology that uses discrete (discontinuous) values. By contrast, analog (non-digital) systems use a continuous range of values to represent information. Although digital representations are discrete, they can be used to carry either discrete information, such as numbers, letters or other individual symbols, or approximations of continuous information, such as sounds, images, and other measurements of continuous systems.

## Slide 3
Inputs and Outputs
An input “receives” information or senses a voltage in the external world.
An output “delivers” information or makes something happen in the external world.
living with the lab
Below is an example from an earlier class where we made an LED flash on and off.
Are we using digital pin 0 as an input or an output?
void setup() {
pinMode(0, OUTPUT);
}
void loop() {
digitalWrite(0, HIGH);
delay(1000);
digitalWrite(0, LOW);
delay(500);
}
digital output

## Slide 4
living with the lab
Receiving Input from an Arduino
int val;
val = digitalRead(7);
int val;
val = analogRead(5);
digital input
analog input
val is either 0 or 1
0 = voltage sensed at digital pin 7 is LOW (0V)
1 = voltage senses at digital pin 7 is HIGH (5V)
val is an integer between 0 and 1023
0 = voltage sensed at analog pin 5 is zero volts
1023 = voltage senses at analog pin 5 is five volts
Guess what val would be if the voltage sensed at analog pin 5 was 2.5V?
511

## Slide 5
living with the lab
Digital Inputs
The Arduino reference indicates that digitalRead() will return . . .
  a value of HIGH if the voltage at the digital input pin is greater than 3 volts
  a value of LOW if the voltage at the digital input pin is less than 2 volts.
time (milliseconds)
voltage (V)
0 1 2 3 4 5 6 7 8 9
5
4
3
2
1
0
digitalRead()returns LOW or 0
digitalRead()may return a value of HIGH or LOW
digitalRead()returns HIGH or 1
LOW or HIGH???
low
high
ambiguous

## Slide 6
living with the lab
Analog Inputs
The analog input pins on your Arduino have 10-bit resolution and consequently measure in (2)10 or 1024 increments.
The analogRead() functions returns a value between 0 and 1023, where 0 is zero volts and 1023 is 5 volts.
smallest increment of voltage that can be read = 0.00488 volts

## Slide 7
living with the lab
data point from plot above | If a digital pin is used to sample voltage | if an analog pin is used to sample voltage | 
 | output of digitalRead() | hypothetical analogRead() output | voltage computed from analogRead() output
time (milliseconds)
voltage (V)
0 1 2 3 4 5 6 7 8 9
5
4
3
2
1
0
digitalRead()returns LOW or 0
digitalRead()may return a value of HIGH or LOW
digitalRead()returns HIGH or 1
point 1
point 2
point 3
Examples
2
ambiguous
526
1
0
217
3
1
964