## Slide 1
Photoresistor
resistance changes dramatically with light level
living with the lab
Using Photoresistors with an Arduino
© 2011 LWTL faculty team

## Slide 2
implement photoresistor and LED circuits
living with the lab
5V
analog input 3
photoresistor
10kW
330Ω
digital pin 11

## Slide 3
living with the lab
int photo_pin = 3; // Analog input pin for photoresistor
int LED_pin = 11; // Digital output pin for LED
void setup() {
Serial.begin(9600); // Open serial communication w/ host PC
pinMode(LED_pin,OUTPUT); // Configure LED_pin for output
}
void loop() {
int val = 0; // Stores reading of analog input
val = analogRead(photo_pin); // Read voltage on photo_pin
Serial.println(val); // print value to serial monitor
if(val < 600) { // if statement used to control LED
digitalWrite(LED_pin,HIGH); delay(100);
digitalWrite(LED_pin,LOW); delay(100);
}
}
enter and run the following sketch

## Slide 4
if statement details
living with the lab
if (x > 50)
{ // do something here }
comparison operators
x == y x is equal to y
x != y x is not equal to y
x < y x is less than y
x > y x is greater than y
x <= y x is less than or equal to y
x >= y x is greater than or equal to y
arduino.cc