## Slide 1: Cross-Country Sit Ski
Cody Barnett
Betsy Camp
Josh Metzler
Robbie Quesada
Mark Scheel
Alex Triplett
Academic Advisor: Dr. Hormoz Zareh
Industry Advisor: Jennifer Armbruster
Sponsor: PSU Inclusive Recreation

## Slide 2: Agenda
Project Background
Key Design Requirements
External Search
Final Design
Design Analysis
Product Testing
Notes: Agenda
  What we are going to talk about
  Take you through what our customer needs, our design process, and talk about our final product

## Slide 3: Project Background
What is a sit ski?
  Enables user to ski from a seated position
  Cross country and downhill models
Notes: Project Background
  What is a sit ski? A device that allows user to ski from a seated position
    Used by people in wheelchairs
      Quadriplegics, paraplegics, amputees, and people with MS

## Slide 4: Project Background
Sponsored by the Inclusive Rec Department at PSU
  Want a versatile sit ski that can accommodate a wide range of user injuries
Notes:   Primary Customer
    Inclusive Rec Department at PSU
  Dept wants a sit ski available to users who are interested in trying the sport
    Most sit skis custom built to a specific injury
    Dept funding for equipment is limited, so Inclusive Rec tasked our team to design and build a single sit ski that could be used by the widest possible range of users
  Sit ski had to accommodate spinal injuries from the T12 to C5 vertrabrae (explain photo)
    Main difference is the amount of abdominal functionality a person has – as spinal injury goes higher, upper body function decreases
      Amount of arm hand hand functionality decreases with higher level spinal injuries too
    Sit skiers with high level injuries don’t have much abdominal strength and will likely need to be secured to seat back
    Sit skiers with lower level injuries will probably choose to be free of the seat back so they can lean forward and put core strength into propulsion

## Slide 5: Mission Statement
  The objective of the PSU Sit Ski Team is to design and build a cross-country sit ski for the PSU Inclusive Rec Department. The sit ski must accommodate varying user size, weight, and injury type. The product and supporting documentation will be delivered to Inclusive Rec in June of 2012.

## Slide 6: Key Design Requirements
Seat back height adjusts from 20” to 25”
Seat back reclines from 90° to 100°
Bottom of seat adjusts from 0° to 10°
Footrest adjustable
Restraints for T12 to C5 injuries
Cost less than $1500
Notes: Key Product Design Specifications
  Adjustability and versatility take precedence over performance
  Took input from Inclusive Rec and made quantifiable design requirements:
    Seat back adjusts from 20” to 25”
    Seat bottom adjusts from 0deg to 10deg
    Seat back reclines from 90deg to 100deg
    Footrest adjustable
    Restraints for T12 to C5 injuries
      Lap and foot belts w/ optional torso restraints
    Cost less than $1500
    Weigh less than 20lb
      Not a key requirement…

## Slide 7: External Search
Teton Nordic Sit Ski
  Telescoping footrest
  Molded seat is fitted to specific user
  Frame is custom-built

## Slide 8: External Search
Central Cross Country Ski
  Footrest inadequate
  Restraints do not accommodate higher-level injuries
  Users have noted rubbing issues with seat material

## Slide 9: Final Design
Notes: Final Design
  (Show CAD model and actual model on same slide)
  Details about construction
    A welded aluminum frame (6061 T6 Al)
      Gussets for reinforcement
    Avoided tube bending in the design to save on cost and specialized manufacturing
    Used welded bushings in tubes that would be bolted or pinned
      Thanks to Evan Waymire and staff at Treske Precision for reviewing our design
    Pinned connections help to make adjustability
    Determined ideal frame dimensions, making compromises on conflicting design requirements:
      Seat height should be fairly close to the same as a wheelchair to facilitate easy transfer
      Get a more efficient pole stroke when user is higher off the ground
      Too high of a seat starts to present a tipping hazard
      Seat width also must make compromises between ergonomics and safety
        Survey of users indicated a narrower sit ski made it eaiser to use poles effectively
        Wider ski was better for stability
    Delrin bushings aid in telescoping feature of the seat back
      Reduce slop
    Hand brake was not initially requested by the customer, but team determined it to be an important safety feature – inlusive rec agreed
    Powder coated frame
      Seat back tubes were anodized because of the moving parts

## Slide 10: Theoretical Analysis
Types of engineering analysis leading to final design
  Finite Element Analysis
  Tip analysis
  Ergonomic analysis
  Weld analysis
  Tube bending analysis
  Tube buckling analysis
Notes:   Details about theoretical analysis (show figures and FEA pictures)
    Stability analysis to determine ideal frame dimensions
    Max stresses in the seat back – seat back will likely be used to push the sit ski; team determined the safety factor wrt max loads the seat will be subjected to
    Looked at stresses in the seat bottom given the max user wt
    Used finite element software to test support member configurations in the frame; determined maximum deflection and internal stresses
    Examined the frames suceptibilty to bucking
    Determined FS wrt shear in key load bearing adjustability pins
    Determined stresses in the welds of the hand brake when put to use

## Slide 11: Adjustability
Seat back adjusts from 20” to 25”

## Slide 12: Adjustability
Seat back reclines from 90° to 100°

## Slide 13: Adjustability
Bottom of seat adjusts to 10°

## Slide 14: Adjustability
Footrest adjustable

## Slide 15: Product Evaluation
Specified adjustability
Restraints for T12 to C5 injuries
Total cost less than $1500
Weight less than 20lb
Pass
Pass
Pass
Fail
Notes:       Specified Adjustability
      Restraints for T12 – C5
      Cost less than $1500
      Less than 20lb
        Fails, but we knew or design was sacrificing performance for the sake of comfort and adjustability. We can live with this failure.

## Slide 16: Field Testing
Field testing at Mt Hood…

## Slide 17: Field Testing
Verified tipping angle of the sit ski

## Slide 18: Field Testing
Collapsed for storage and transport

## Slide 19: Sponsors
Keen
  Restraints
  Head rest
  Seat Cushion
Next Adventure
  Discounted skis and bindings
Treske Precision Machining
  Donated fabrication labor
Finish Line Industries
  Donated powder coating and other material finishes

## Slide 20: Questions?