## Slide 1: Bamboo Bike Capstone Team Members Camrun Arkills Kyle Heitmeyer Fay Gibson Matt Brown Faculty Advisor Hormoz Zareh , PhD Associate Professor of Mechanical Engineering
Industry Advisor
Alexi Lamadrid
Owner, Bamboo’d Gear

## Slide 2: Outline
Mission Statement
Product Design Specification
Final Design
Design Evaluation
PDS Evaluation
Q & A

## Slide 3: Mission Statement
To design and construct a low cost, reliable, and desirable bike frame compatible with off the shelf components made from bamboo stalks.

## Slide 4: PDS Summary
Build frame and assemble components in 25 man hours or less
Stay within a $155 budget for frame parts and materials
Assure the bike can support riders of various sizes
The bike must be aesthetically pleasing to the eye

## Slide 5: Current Design
Bamboo tubing
Joints wrapped with hemp strands soaked in an epoxy resin
Metal inserts for seat tube, bottom bracket, dropouts and headset.
~50 hrs build time
Single Gear Drive Train
Parts Cost ?????

## Slide 6: Final Design
Bamboo tubing
Joints wrapped in carbon fiber strips coated in an epoxy/hardener resin
Metal inserts for seat tube, bottom bracket, dropouts and headset.
~10 hr build time
Gear Drive Train ????
Parts Cost $139

## Slide 7: Design Evaluation Bamboo
Pros
  Highly sustainable
  Produces 35% more oxygen and absorbs 4x the CO2 than hardwood trees
  High Strength
    ~30,000 psi in tension
    ~14,000 psi in compression
Cons
  Heavier frame weight compared to its aluminum counterpart
  Mechanical properties vary between species

## Slide 8: Carbon Fiber Webbing
Pros:
  High Strength
  Low Weight
  Wider strands allow quicker wrapping time
Cons:
  Not readily available in small quantities
  Expensive

## Slide 9: Super Sap CLR Epoxy w/FAST Hardener
Pros
  Made from biobased renewable materials
  UV Stability
  High Tensile and Compression Strength
Cons
  7 day recommended cure time
  Can be hazardous if proper safety precautions are not met
  48 oz Kit - $47.95

## Slide 10: Jig Assembly
Pros
  Upright position allows for easier access to entire frame
Cons
  Wood support board is less sturdy and requires holes to be drilled manually to attach jig components

## Slide 11: PDS Evaluation
Requirements | Goal | Actual
Assembly Time | < 25 hours | 10 hours
Budget | < $155 | $139
Rider Capacity | ??????? | ?????
Aesthetics | Easy on the eyes | You be the judge!

## Slide 12
Questions??