## Slide 1: VGO CABINET CYCLE TESTER
HANNY SELBAK
AMMAR AL SALMAN
DRAGAN ULEMEK
JOHN GEILE

## Slide 2: PDS
Be able to run a 25000 cycle test
Adjustable length settings for varying drawer/cabinet set-ups
Able to support a load of 15 lbs/sq ft drawer area
3-5 year life-time (depending on frequency of usage)
3 second cycle time
Smooth open and close motion

## Slide 3: MOTION DEVICE SELECTION
The criteria for motor selection was organized as shown below. VGO currently uses a pneumatic actuator. We have chosen to go with a
DC MOTOR.

## Slide 4: POSSIBLE DESIGNS Need to translate rotational motion (DC Motor) to linear motion.
Left to Right: scotch yoke, rack and pinion, worm drive

## Slide 5: LINEAR DRIVER SELECTION
The criteria for driver selection was organized as shown below. VGO currently uses a piston in conjunction with the pneumatic actuator. We have chosen to go with a WORM GEAR.

## Slide 6: WORM DRIVE SELECTION
POWER SCREW
Higher friction
Lower max speeds
Lifetime is inconsistent
BALL SCREW
Quiet motion
High speeds
Very low friction
Not self-locking

## Slide 7: WORM GEAR WITH BALL SCREW

## Slide 8: SYSTEM CONTROLLER
An Arduino Due was chosen to control the system. It is easily programmable, low-cost ($40-$50), and can support multiple inputs/outputs.
32-bit, 84 MHz processor, 54 digital input/output pins

## Slide 9: CONTROL SYSTEM
Used a proportional controller
Feedback is from rotary encoder on worm screw
  400 pulses per rev
Encoder senses any outside interaction
Motor voltage is varied to match desired position

## Slide 10: DERIVED MOTION
Maximum displacement, velocity, acceleration, and force of the system.
Rotary motion of the worm drive with respect to the linear position of the drawer.

## Slide 11: SYSTEM PROPERTIES
1 Test = 1.8 million revolutions maximum
40 Tests/year for 5 years = 360 million revolutions
Maximum torque required to open drawer = 15 oz-in
Maximum axial force = 10 lb
The system design is meant to outlast this with minimal maintenance/replacement parts

## Slide 12: ENGINEERING THEORETICAL DESIGN
FS MAX TOURQE 7
FS BUCKLING 32
FS FATIGUE LIFE 411

## Slide 13: CURRENT STATUS
DESIGN COMPLETED
CONSTRUCTION COMPLETED
FINAL TESTING
FUTURE ACTIONS
          DELIVER TO CUSTOMER

## Slide 14: THANK YOU!
QUESTIONS?