## Slide 1: Voltage Drops Around Closed Loops
470W
220W
5V
-
+
220W
living with the lab

## Slide 2
Select Resistors
Find the 220W and the 470W resistors from your parts kit.
Now, find the 220W resistor.
Example: 470W resistor
4 = yellow
7 = violet
Add 1 zero to 47 to make 470, so 1 = brown
So, 470 = yellow, violet, brown
color | digit
black | 0
brown | 1
red | 2
orange | 3
yellow | 4
green | 5
blue | 6
violet | 7
gray | 8
white | 9
first
digit
second digit
number
of zeros
tolerance
gold = ±5%
silver = ±20%
living with the lab

## Slide 3
Build the Series Circuit Below
470W
5V
-
+
220W
living with the lab
5V
220W
470W
5V
+
-
220W
470W
All of these circuits are the SAME!!

## Slide 4
Compute the Voltage Drops Across the Two Resistors
Use Ohm’s Law: V = I · R
Now, add the voltage rise of the power source (+5V) to the voltage drops across the resistors (negative numbers).
living with the lab
V1=5V
+
-
R1 = 220W
R2 = 470W
given
find the equivalent resistance
find the current
find the voltage drop across R1
find the voltage drop across R2

## Slide 5
Use Multimeter to Measure Voltages Around Loop
(1) From 5V pin to Gnd
(2) Across the 220W resistor
(3) Across the 470W resistor
Remember . . .
a RESISTOR is a voltage DROP and
a POWER SOURCE is a voltage RISE
DV1 = _____
DV2 = _____
DV3 = _____
D V1 - DV2 - DV3 = _____
rises must balance drops!!!!
living with the lab
5V
+
-
220W
470W

## Slide 6
Compare Measurements to Theory
Pretty close!
living with the lab
DV = 3.41V
DV = 1.59V
V1=5V
+
-
R1 = 220W
R2 = 470W

## Slide 7
Kirchoff’s Voltage Law (KVL)
Kirchoff’s Voltage Law says that the algebraic
sum of voltages around any closed loop in a
circuit is zero – we see that this is true for our
circuit. It is also true for very complex circuits.
Notice that the 5V is DIVIDED between the two resistors, with the larger voltage drop occurring across the larger resistor.
living with the lab
5V
V1=5V
+
-
R1 = 220W
R2 = 470W
DV = 3.41V
– 3.41V
DV = 1.59V
– 1.59V
= 0

## Slide 8
Gustav Kirchoff (1824 – 1887) was a German physicist who made fundamental contributions to the understanding of electrical circuits and to the science of emission spectroscopy. He showed that when elements were heated to incandescence, they produce a characteristic signature allowing them to be identified. He wrote the laws for closed electric circuits in 1845 when he was a 21 year-old student.
Photo: Library of Congress
living with the lab