## Slide 1: Self-organization of Wireless SensorSelf-organization of Wireless Sensor Networks for Wildfire Detection Using Shapley Values Self-organization of Wireless Sensor Networks for Wildfire Detection Using Shapley Values Networks for Wildfire Detection Using Shapley Values
Garrison Greenwood
Dept. of Electrical & Computer Engineering
Portland State University
Portland, OR 97201 USA

## Slide 2
Wildfires are uncontrolled and unplanned fires that destroy vegetation (forests, bushland, etc.) and animal species.
In the United States about 8 million acres, on average, burned each year in wildfires between 2017 and 2021 with an annual expenditure of $2.5 billion (in 2020 dollars) on fire suppression activities.
Although wildfires do have positive effects on many ecosystems, their high economic costs and adverse human health effects can be staggering.

## Slide 3
Early detection of wildfires can help minimize those negative effects.
Environmental monitoring should be effective, yet non-intrusive, non-toxic and as inexpensive as possible.
Unfortunately, monitoring in remote, limited-access areas is difficult…
Wireless sensor networks (WSNs) can meet those requirements.

## Slide 4: Wireless Sensor Networks (WSNs)
Multiple sensors (100s or 1000s) cooperatively collect data about a physical environment.
Data is wirelessly sent to a base station.
The base station can locally use the data or serve as a gateway that sends the collected data to other networks (e.g., the internet)
Sensor nodes are randomly distributed (for example by air) in remote areas.

## Slide 5
The network model
Sensor nodes are low cost by design and have a limited transmitter power output.
Consequently, most sensor nodes do not have a 1-hop communication with the sink node.
One solution is to organize nodes into clusters

## Slide 6
The sink node is located at a known location and is not energy limited. It communicates with all nodes within R0 meters.
For sensor nodes we assume
- sensor batteries have finite capacity and are not rechargeable. - sensor locations are not known (randomly dispersed by air) - sensors can communicate with neighbor nodes located within R1 meters (R1 < R0). - sensors can adjust their transmitter output power. - all nodes are homogeneous so they can act as sensors or cluster heads.

## Slide 7
After deployment, the sensors must self-organize, that is, organize itself into clusters autonomously.
Self-organization creates the WSN.

## Slide 8
Shapley’s Problem
Lloyd Shapley* was interested in the following coalition problem:
Problem Statement
A coalition C ⊂ N cooperates to complete some activity.
When the activity is finished, there is a profit to distribute among the | C |
coalition members.
What a fair distribution of the profit among the coalition members?
*2012 recipient of the Nobel prize in economics sciences
12

## Slide 9
What is a fair distribution?
Intuitively, a fair distribution would be an equal payoff to everyone.
Example
Three people want to build a house, sell it, and split the profit.
·one person does all of the plumbing and internal wiring
· one person installs the doors and windows
· one person lays the foundation, puts up the walls and roof and connects all utilities (water, sewer, etc.)
Question: How would you determine a fair distribution of the profit in this
example?

## Slide 10
Shapley Values
Shapley believed a fair distribution must consider the marginal contribution
of an individual—i.e., the value that individual adds to a coalition by joining it.
The marginal contribution of an individual joining a coalition C can be
positive, negative, or zero depending on whether the larger C has more,
less, or the same value.
A weighted sum of marginal contributions for an individual over all possible
coalitions is called the Shapley value for that individual.

## Slide 11
Shapley Value (cont.)
The Shapley value for an individual is a weighted sum of the marginal
contributions over all possible coalitions.
Let C ⊆ N be a coalition with n = | N | .
Definition
The Shapley value of individual i ∈ C is
is a characteristic function which gives the value of the coalition C
(problem dependent).
18

## Slide 13
Unmark all nodes
Sink node broadcasts alert message; all nodes within distance d < R0 respond
Sink nodes selects subset of responding nodes as cluster heads (CHs)
CHs broadcasts alert message; unmarked all nodes within distance d < R1 < R0 respond
Nodes responding to CH(k) are marked and join the cluster
Marked cluster nodes broadcast alert message; all marked nodes within distance d < R1 respond. Nodes record ID numbers of responders.
Shapley values (SVs) are computed for each node in the cluster
Node with the smallest SV re-designated as a CH that will form a new cluster
If not all nodes in a cluster, go to step 4.

## Slide 14
,
is the cardinality of its coalition set = 2
,
is the cardinality of union of the coalition sets = 4

## Slide 15
Nodes 1 and 2 had the same lowest Shapley values

## Slide 18
Summary
This paper presents a self-organization method for WSNs. Method is well suited wild-fire detection (or any other application) in remote, inaccessible areas.
No sensor node localization is required; nodes determine neighbors by ability to communicate.
All comunication between clusters is 1-hop
Shapley values determine suitable cluster heads for forming new clusters
Routing paths from clusters to the sink node are defined when the clusters are created.

## Slide 19
Questions