## Slide 1: Lecture 12
Topics
  Modular Design
  Adder and Subtractor Design
  Multiplier Design
  ALU Design

## Slide 2: Adders and Subtractors

## Slide 3: The Half Adder
A0
+ B0
CO1 S0
A0 B0 C01 S0
0 0 0 0
0 1 0 1
1 0 0 1
1 1 1 0

## Slide 4: Half Subtractor
A0
- B0
BO1 D0
A0 B0 B01 D0
0 0 0 0
0 1 1 1
1 0 0 1
1 1 0 0
Contrast with Half Adder: same equation for D0! But BO1 and CO1 are different. Must complement A0. Can build HS from HA by
Inverting A0, then inverting S bit to correct.

## Slide 5: The Full Adder
Consider a circuit to add two 4-bit numbers:
A3 A2 A1 A0
+ B3 B2 B1 B0
CO4 S3 S2 S1 S0
Truth table would have 8 inputs (28 = 256 rows) and 5 outputs,
requiring 5 minimized functions (5 8-variable K-maps).
But operation at each bit position (after A0/B0) is identical:
COi
Ai
+ Bi
COi+1 Si
“bit slice”

## Slide 6: Full Adder Truth Table
CI A B CO S
0 0 0 0 0
0 0 1 0 1
0 1 0 0 1
0 1 1 1 0
1 0 0 0 1
1 0 1 1 0
1 1 0 1 0
1 1 1 1 1

## Slide 7: Ripple Carry Adders

## Slide 8: Ripple Carry Adder
A1 A0
+ B1 B0
CO2 S1 S0

## Slide 9: Modular Two Bit Adder/Subtractor
This is one of the reasons we choose 2s complement for representing negative numbers!
Increment and decrement
Increment: +1 (just use CI)
Decrement: -1 (use all 1s)

## Slide 10: XOR Application: Twos Complement
4 bit adder/subtractor circuit from Chapter 1 showing XOR to form twos complement (RC)

## Slide 11: Propagation Delay in Ripple Adder
Assuming S is
implemented using
AND, OR, NOT
S: Tpd = 3 tp
CO: Tpd = 2 tp
Can use HA for first bit and knock off 1 Tp

## Slide 12: Partition Carry-Out Logic
Settling time for n stage ripple adder
ST = 3tp + (n-1)(2tp) = (2n+1)tp
S of MSB stage
C of remaining earlier n-1 stages
Let’s look at what happens if we pull the carry-out portion of the logic out of the FA…
If we use HA the CO1 is computed by a single AND gate (Tp)

## Slide 13: Using HA for LSB Stage
If we use HA for 1st stage (no CI)
ST = 3tp + (n-2)(2tp) + tp = (2n)tp

## Slide 14: Carry Look Ahead Adders

## Slide 15: Carry Look-Ahead Adder
Con+1 logic not dependent upon entire prior stage (COn) logic

## Slide 16
G (carry generate) is dependent upon current stage's ability to generate a carry.
P (carry propagate) is dependent upon current (and prior) stages’ ability to propagate a carry.
A carry is generated at a stage i if it is generated by stage i’s inputs (Ai,Bi) or by any prior stage and propagated by every succeeding stage.
We can re-arrange the Cout equation, a defining G = A & B and P = A + B to get…
Intuitively, you can think of it in this way…
Alternatively, you can back substitute and observe that because we can generate all the P and G terms in one Tpd we are no longer dependent on Cout of previous stage

## Slide 18: Carry Look-Ahead Adder
Con+1 logic not dependent upon entire prior stage (COn) logic
Uses: G0 through Gn-1 and P1 through Pn-1
Settling Time = 6tp (constant) for 3 or more stages
Look closely at Tpd – not cumulative through the carry look-ahead part.
Doesn’t use previous carry-out stage

## Slide 19: Speed Up Improvement
Ripple Carry Adder (n) Stages using HA for LSB
(2n)Tp
Carry Look-Ahead Adder (n) Stages (using SOP)
6Tp
Speed up for n stage adder
((2n)Tp-6Tp)/(2nTp)
Assume Tp =1 and 4 stages:
(2 x 4 – 6)/(2 x 4)=
=2/8
=25%
Conclusion
Assuming Carry Look-Ahead we have 25% speedup for 4 stages

## Slide 20: Speed Up Improvement
Ripple Carry Adder (n) Stages using HA for LSB
(2n)Tp
Carry Look-Ahead Adder (n) Stages (using SOP)
5Tp
Speed up for n stage adder
((2n)Tp-5Tp)/(2n)Tp)
Assume 4 stages
(2 x 4 – 5)/(2 x 4)
3/8
37.5%
Conclusion
Assuming Carry Look-Ahead we have 37.5% speedup for 4 stages
changed

## Slide 21: Limits to Speed Up
Carry generation G0 of first stage must be capable of driving all succeeding stages
Each succeeding stage requires gates with increasing number of inputs (fan-in)
Gate count increases with each stage

## Slide 22: Expandable Carry Look-Ahead Adder
74LS83A & 74LS283
74LS83A: change slide after checking Wakerly? Actual device sum is 24ns and carry is 17 and gate equivalent description confirms 4 Tpd for Sum, 3Tpd for CO4. Carry look ahead used internally.

## Slide 23: Wallace Trees

## Slide 24: Carry-Save Adders (Wallace Tree Summing Network)
A0
B0
+ C0
S10
CO11
+ D0
S21 S20
CO21
+ E0
S31 S30
CO32 CO31
+ CO42_________
S42 S41 S40
Adding more than two operands with full adders (A,B,CI,CO)

## Slide 25: Carry-Save Adders

## Slide 27: Multipliers

## Slide 28: Multiplier Design
M x N bit multiplier requires M+N bit result: 2M x 2N = 2M+N
Consider a 2-bit x 2-bit binary multiplier
11
x11
11
+ 11..
1001
multiplicand
multiplier
partial product 0
partial product 1
result
Truth tables quickly become unmanageable –use modular approach
Every partial product can be obtained from an AND operation
Use ripple or carry look-ahead adder to add two sets of partial products
Use carry save adder to add more than two sets of partial products
A0 B0 A0xB0 A0×B0
0 0 0 0
0 1 0 0
1 0 0 0
1 1 1 1

## Slide 29: Example: 3-bit x 3-bit Multiplier Using Ripple Adders

## Slide 30: Example: 3-bit x 3-bit Multiplier Using Ripple Adders
multiplicand
multiplier
partial product 0
partial product 1
partial sum 0
partial product 2
partial sum 1 (result)
9 partial products (9 AND gates)
2 rows of adders
Pmn = Am x Bn
A2 A1 A0
x B2 B1 B0
P20 P10 P00
+ P21 P11 P01……..
S40 S30 S20 S10 S00
+ P22 P12 P02………………..
R5 R4 R3 R2 R1 R0

## Slide 31: Multiplier Using Ripple Carry Adders

## Slide 32
multiplicand
multiplier
partial product 0
partial product 1
partial sum 0
partial product 2
partial sum 1 (result)
Pmn = Am x Bn
A2 A1 A0
x B2 B1 B0
P20 P10 P00
+ P21 P11 P01……..
S40 S30 S20 S10 S00
+ P22 P12 P02XXXXXXXX
R5 R4 R3 R2 R1 R0
Using ripple carry adder

## Slide 33: Example: 3-bit x 3-bit Multiplier Using Carry Save Adder

## Slide 34: Multiplier Using Carry Save Adder
Can use the Wallace Summing Tree (Carry Save) Adder

## Slide 35: ALUs – Arithmetic Logic Units

## Slide 36: ALUs – Arithmetic Logic Units
M S0 F and CO Comment
0 0 A+CI Increment A if CI == 1
0 1 A+B+CI Add A+B with carry
1 0 A OR B A OR B
1 1 A Å B A XOR B
Computational heart of a computer
M (mode) selects arithmetic or logic mode
S (select) selects operations
1-bit slice (because of CO, capable of being expanded)

## Slide 37: Modular ALU Implementation
M S0 F and CO
0 0 A+CI
0 1 A+B+CI
1 0 A OR B
1 1 A Å B

## Slide 38: ALUs – Arithmetic Logic Units

## Slide 39: Hierarchical Implementation of 16-bit ALU

## Slide 40: Hierarchical Implementation of 16-bit ALU

## Slide 41: Hierarchical Implementation of 16-bit ALU
16
16
…

## Slide 42: Still Better…
module ALUnBit(F,CO,A,B,CI,M,S);
parameter nBITS = 16;
input [nBITS-1:0] A,B;
input CI, M, S;
output [nBITS-1:0] F;
output CO;
wire C[nBITS:0];
genvar i;
assign C[0] = CI;
assign CO = C[nBITS];
generate
for (i=0; i < nBITS; i = i+1)
begin:ALU
ALUSlice m (F[i],C[i+1],A[i],B[i],C[i],M,S);
end
endgenerate
endmodule

## Slide 43: Parameters
module ALUnBit(F,CO,A,B,CI,M,S);
parameter nBITS = 16;
input [nBITS-1:0] A,B;
input CI, M, S;
output [nBITS-1:0] F;
output CO;
wire C[nBITS:0];
genvar i;
assign C[0] = CI;
assign CO = C[nBITS];
generate
for (i=0; i < nBITS; i = i+1)
begin:ALU
ALUSlice m (F[i],C[i+1],A[i],B[i],C[i],M,S);
end
endgenerate
endmodule
module Processor(…);
ALUnBit ALUa (…)
ALUnBit #(32) ALUb (…);
.
.
.
ALUnBit #(64) ALUc (…);
endmodule
Creates three instances of ALUnBit – one using nBITS = 16 (default), another using nBITS = 32, and another using nBITS = 64
Can have multiple instances (each of different sizes)!

## Slide 44: Parameters
module RAM(
clk , // Clock Input
address , // Address Input
data , // Data bi-directional
cs , // Chip Select
we , // Write Enable/Read Enable
oe // Output Enable
);
parameter DATA_WIDTH = 8 ;
parameter ADDR_WIDTH = 8 ;
parameter RAM_DEPTH = 1 << ADDR_WIDTH;
// Actual code of RAM here
endmodule
module RAMcontroller ();//Some ports
RAM #(.DATA_WIDTH(16),
.ADDR_WIDTH(8),
.RAM_DEPTH(256)) R1(clk,address,data,cs,we,oe);
endmodule

## Slide 45: ALUs
32-bit ALU
Typical ALU Operations

## Slide 46: Sources
Prof. Mark Faust
John Wakerly