## Slide 1: Lecture 13
Topics
  Latches
  Flip Flops
  Algorithmic State Machines

## Slide 2: Latches

## Slide 3: Possible States for Light Switch

## Slide 4: S-R Latch
S R Q+
0 0 Q
0 1 0
1 0 1
1 1 0
S-R latch is reset dominant
Different ways to name/nomenclature for current/next state. Text uses Q+ for next.

## Slide 5: Alternative Nomenclature for latches
Present State Next State
Output Symbol Output Symbol
Q Q
Q Q(t+1)
Qt Q(t+1)
Qn Q(n+1)
Q0 Q
Y Y+
y Y

## Slide 6: S-R Latch States
S-R latch is
reset dominant

## Slide 7: Characteristic Equations

## Slide 8: Present State/Next State Table (PS/NS)

## Slide 9: Timing Diagram

## Slide 10: Races
Critical Race
Non-critical Race

## Slide 11: Races
Just as we used K-maps to not only reduce Boolean equations but to detect hazards, we can use K-maps to analyze anomalous latch behavior as well.
Race is when two or more inputs change simultaneously.
May or may not be a critical race.
Depends upon the behavior of the circuit.

## Slide 12: Races
Critical race:
We start in State represented by minterm m3. (stable state) Q is 0, SR are 11s.
Both S and R are transitioning to 0.
Notice we take different paths through the K-map depending upon whether R or S transitions first.
If S transitions first, we transition to state m0 where Q+ remains Q (no transitions on output).
However, if R transitions first, we attempt to set the latch, resulting in Q+ = 1.
Then, when S transitions we go to state m4.
Not only do we end up in different states, but we have different values on the Q output – all depending upon minor differences in relative timing between transitions on S/R.
This is a critical race.

## Slide 13: Races
Non-critical race:
Start in state m6 (stable) with SR 10. Both S and R are going to change.
If S changes first, we go to state m4 (a stable state) with no transition on output.
Then when R changes we transition to state m1, also a stable state, and with an output of 0.
If R changes first, we transition to state m3, a stable state with a transition to 0 on output.
When S subsequently changes we transition to m1, another stable state where Q remains 0.
Non-critical race – OK and correct behavior regardless of which signal transitions first.

## Slide 14: Metastable State
An often overlooked condition in which the output can remain in an illegal (even oscillating) state for an indeterminant period of time.
Metastability can be caused by a runt pulse (a positive or negative pulse which never achieves either a value of a 1 or 0). This can occur when two inputs to a gate change near simultaneously (see hazards earlier).
Metastability can also when two inputs to a latch change near simultaneously.
Condition also arises when synchronizing with external events (e.g. asynchronous inputs to synchronous finite state machines).

## Slide 15: State Machines

## Slide 16: State Diagrams
S R Q+
0 0 Q
0 1 0
1 0 1
1 1 0
S R Q Q+
0 0 0 0
0 0 1 1
0 1 0 0
0 1 1 0
1 0 0 1
1 0 1 1
1 1 0 0
1 1 1 0

## Slide 17: Algorithmic State Machines (ASM)

## Slide 18: Clock (Oscillator) Circuit
PS/NS Table
K-map
State Diagram
Delay Model

## Slide 19: Clock Waveforms
Delay
  Buffers
  Additional (maintain odd number) inverters
  RC circuit
  Crystal Oscillator

## Slide 20: Gated Sequential Circuits
Addition of control input
  Gated Latch (Level Activated)
  Edge-Triggered Flip Flop
  Pulse Triggered Flip Flop

## Slide 21: Gated SR Latch

## Slide 22: Gated SR Latch Using NANDs

## Slide 23: Gated D Latch
D Q+
0 0
1 1
D Latch is Hazard Free (product terms chain-linked)

## Slide 24: Gated D Latch Timing

## Slide 25: Use as Storage Elements

## Slide 26: Flip Flop Circuits
Pulse Narrowing Circuit
Explain pulse-narrowing circuit. Attach as front end to D flip flop’s C input.

## Slide 27: Edge-Triggered D Flip Flop

## Slide 28: Manual Reset of D Flip Flop

## Slide 29: 74LS74A

## Slide 30: JK Flip Flops
J K Q+ Comment
0 0 Q No change
0 1 0 Reset
1 0 1 Set
1 1 Q Toggle

## Slide 31: T Flip Flops
J = K=T Q+ Comment
0 0 0 Q No change
0 1
1 0
1 1 1 Q Toggle

## Slide 32: State Diagrams for Binary Up Counters

## Slide 33: 4-Bit Binary Up Counter
T flip flops ideal for counters (remain same or toggle)!

## Slide 34: Counter Timing Diagram

## Slide 35: State Machines
State Transition Diagrams
Next State Tables
Mealy and Moore Machines
  Mealy: Output logic uses current state and inputs
  Moore: Output logic uses only current state
One Hot vs. Encoded State Machines

## Slide 36: Example T-bird tail-lights

## Slide 37: T-bird tail-lights example

## Slide 38: State diagram
Inputs:
LEFT, RIGHT, HAZ
Outputs:
Six lamps
(function of state only)

## Slide 39: Encoded or One-Hot?
Encoded
  8 states
  23 = 8
  Need 3 flip flops
  Need to determine state assignment
One-hot
  Dedicate a flip flop per state
  Need 8 flip flops

## Slide 40: Implementation (Encoded, Moore Machine)
Next
State
Logic
Output
Logic
Inputs
Outputs
Current State

## Slide 41: Output logic
LC = L3 + LR3
LB = L2 + L3 + LR3
LA = L1 + L2 + L3 + LR3
RA = R1 + R2 + R3 + LR3
RB = R2 + R3 + LR3
RC = R3 + LR3
LC = Q2’×Q1×Q0’ + Q2×Q1’×Q0’
LB = Q2’×Q1×Q0 + Q2’×Q1×Q0’ + Q2×Q1’×Q0’
LA = Q2’×Q1’×Q0 + Q2’×Q1×Q0 + Q2’×Q1×Q0’ + Q2×Q1’×Q0’
RA = Q2×Q1’×Q0 + Q2×Q1×Q0 + Q2×Q1×Q0’ + Q2×Q1’×Q0’
RB = Q2×Q1×Q0 + Q2×Q1×Q0’ + Q2×Q1’×Q0’
RC = Q2×Q1×Q0’ + Q2×Q1’×Q0’
Q2
Q1
Q0

## Slide 42: Next State Logic
State transition table for encoded states
Next step depends on implementation choice
  Synthesize or Structural with choice of FFs

## Slide 43: Transition Equations
Q2* = Q2’× Q1’ × Q0’ × (HAZ + LEFT × RIGHT)
+ Q2’ × Q1’ × Q0’ × (RIGHT × HAZ’ × LEFT’)
+ Q2’ × Q1’ × Q0 × (HAZ)
+ Q2’ × Q1 × Q0 × (HAZ)
+ Q2 × Q1’ × Q0 × (HAZ’)
+ Q2 × Q1’ × Q0 × (HAZ)
+ Q2 × Q1 × Q0 × (HAZ’)
+ Q2 × Q1 × Q0 × (HAZ)
Q2* = Q2’× Q1’ × Q0’ × (HAZ + RIGHT)
+ Q2’ × Q0 × HAZ
+ Q2 × Q0

## Slide 44: Transition Equations
Q1* = Q2’ × Q1’ × Q0 × (HAZ’)
+ Q2’ × Q1 × Q0 × (HAZ’)
+ Q2 × Q1’ × Q0 × (HAZ’)
+ Q2 × Q1 × Q0 × (HAZ')
Q1* = Q0 × HAZ’

## Slide 45: Transition Equations
Q0* = Q2’ × Q1’ × Q0’ × (LEFT × HAZ’ × RIGHT’)
+ Q2’ × Q1’ × Q0’ × (RIGHT × HAZ’ × LEFT’)
+ Q2’ × Q1’ × Q0 × (HAZ’)
+ Q2 × Q1’ × Q0 × (HAZ’)
Q0* = Q2’× Q1’ × Q0’ × HAZ’ × (LEFT Å RIGHT)
+ Q1’ × Q0 × HAZ’
No guarantee these are minimal. They certainly aren’t SOP. What we do next depends upon how we’re going to implement the FSM.
Could just give them whole thing to ABEL or some other tool and let it generate minimal SOP.
Also, transition equation isn’t same as excitation equation (unless we’re using D FFs)

## Slide 46: Implementation (Encoded, Moore Machine)
Next
State
Logic
Output
Logic
Inputs
Outputs
Current State
What should the clock’s period be?

## Slide 47: How Fast Can the Clock Be?
Combinational
Logic
Clock
D1
Q
D2
FF tpd
Combinational tpd
FF tsetup
FF 1
FF 2

## Slide 48: Clock Skew
Clock
D1
Q
D2
FF tpd
Combinational tpd
FF tsetup
Even with careful routing, clock will not arrive
at all FFs at the same time. This skew in clock
arrival time affects max clock rate.
Clock Skew
Clock Periodmin = FF tpd + FF tsetup + C tpd + tskew

## Slide 50: One-Hot
IDLE* = IDLE × (HAZ + LEFT + RIGHT)’ + L3 + R3 + LR3
L1* = IDLE × LEFT × HAZ’ × RIGHT’
R1* = IDLE × RIGHT × HAZ’ × LEFT’
L2* = L1 × HAZ’
R2* = R1 × HAZ’
L3* = L2 × HAZ’
R3* = R2 × HAZ’
LR3* = IDLE × (HAZ + LEFT × RIGHT) + (L1 + L2 + R1 + R2) × HAZ
No decoding of state required

## Slide 51: Better Still – Behavioral Verilog
parameter
IDLE = 8'b00000001,
L1 = 8'b00000010,
L2 = 8'b00000100,
L3 = 8'b00001000,
R1 = 8'b00010000,
R2 = 8'b00100000,
R3 = 8'b01000000,
LR3 = 8'b10000000;
reg [7:0] State, NextState;
case (State)
IDLE:
begin
if (Hazard || Left && Right)
NextState = LR3;
else if (Left)
NextState = L1;
else if (Right)
NextState = R1;
else
NextState = IDLE;
end
L1: begin
if (Hazard)
NextState = LR3;
else
NextState = L2;
end
L2: begin
if (Hazard)
NextState = LR3;
else
NextState = L3;
end
L3: begin
NextState = IDLE;
end
R1: begin
if (Hazard)
NextState = LR3;
else
NextState = R2;
end
R2: begin
if (Hazard)
NextState = LR3;
else
NextState = R3;
end
R3: begin
NextState = IDLE;
end
LR3:begin
NextState = IDLE;
end
endcase

## Slide 52: Example: Traffic Light Controller

## Slide 53: Example: Traffic Light Controller
N
S
E
W
Sensors in road detect approaching car on NS and EW roads, generating input signals NScar and EWcar respectively.
Lights are controlled by outputs NSlite and EWlite.
Traffic lights should change only if there is a car approaching from the other direction. Otherwise the lights should remain unchanged.
NScar
EWcar
Clock
Traffic Light Controller
NSlite
EWlite
r

## Slide 54: Example: Traffic Light Controller
r
State assignment
NSgreen = 0
EWgreen = 1

## Slide 55: Example: Serial Line Code Converter

## Slide 56: Example: Serial Line Code Converter
BitIn
BitClock
Clock
Clear
NRZ to
Manchester
Encoder
BitOut
S0
0
S1
0
S3
1
S2
1
0
0
0
1
1
1
fFSM Clock = 2 x fBitClock

## Slide 57: NRZ to Manchester (Moore FSM)
S0
0
S1
0
S3
1
S2
1
0
0
0
1
1
1
Rising edge of BitClock coincides with rising edge of FSM clock.
BitIn changes at falling edge of BitClock
Use falling edge of FSM clock for synchronization (will be at midpoint of bit time) so no danger of sampling BitClock while it’s changing

## Slide 58
//
// Moore FSM for serial line conversion: NRZ to Manchester encoding
//
module NRZtoManchester(Clock, Clear, BitIn, BitOut);
input Clock, Clear, BitIn;
output BitOut;
reg BitOut;
// define states using same names and state assignments as state diagram and table
// Using one-hot method, we have one bit per state
parameter
S0 = 4'b0001,
S1 = 4'b0010,
S2 = 4'b0100,
S3 = 4'b1000;
reg [3:0] State, NextState;
// Update state or reset on every - clock edge
always @(negedge Clock)
begin
if (Clear)
begin
State <= S0;
$display("Reset: S0");
end
else
begin
State <= NextState;
$display("State: %d",State);
end
end
Verilog

## Slide 59
// Outputs depend only upon state (Moore machine)
always @(State)
begin
case (State)
S0: BitOut = 1'b0;
S1: BitOut = 1'b0;
S2: BitOut = 1'b1;
S3: BitOut = 1'b1;
endcase
end
// Next state generation logic
always @(State or BitIn)
begin
case (State)
S0: if (BitIn)
NextState = S3;
else
NextState = S1;
S1: if (BitIn)
$display("S1 Error!");
else
NextState = S2;
S2: if (BitIn)
NextState = S3;
else
NextState = S1;
S3: if (BitIn)
NextState = S0;
else
$display("S3 Error!");
endcase
end
endmodule

## Slide 61: Example: Airplane Gear

## Slide 62: Airplane Gear Example
PilotLever
GearIsUp
Airplane Landing Gear Control
Valve
PlaneOnGround
GearIsDown
Pump
RedLED
GreenLED
  PilotLever Operated by pilot to control landing gear (1:down 0:up)
  PlaneOnGround Sensor 1 when plane on ground
  GearIsUp Sensor 1 when landing gear fully up
  GearIsDown Sensor 1 when landing gear fully down
  TimeUp 1 when two second timer expired
  Valve Controls position of valve (1:lowering 0:raising)
  Pump Activates hydraulic pump (1: activate)
  ResetTimer 1 to reset count-down timer, 0 to count
  RedLED Indicates landing gear in motion
  GreenLED Indicates landing gear down
Do not retract landing gear if plane on ground
Plane should be airborne two seconds before retracting gear
TimeUp
Timer

## Slide 63: Airplane Landing Gear Example
Lever
GearUp
Airplane Landing Gear Control
Valve
OnGround
GearDown
Pump
RedLED
GreenLED
  Lever Operated by pilot to control landing gear (0:down 1:up)
  OnGround Sensor 1 when plane on ground
  GearUp Sensor 1 when landing gear fully up
  GearDown Sensor 1 when landing gear fully down
  Valve Controls position of valve (0:lowering 1:raising)
  Pump Activates hydraulic pump
  RedLED Indicates landing gear in motion
  GreenLED Indicates landing gear down
Do not retract landing gear if plane on ground
Respond to changes in lever position (in case plane started with lever in up position)
Plane should be airborne two seconds before retracting gear

## Slide 64: State Transition Diagram
Waiting for TakeOff
Waiting for Timer
Gear Up
Raising Gear
Lowering Gear
~PlaneOnGround
PlaneOnGround
TimeUp && ~PilotLever
GearIsUp
~PilotLever
PilotLever
PlaneOnGround
Reset
State | Reset Timer | Pump | Valve | RedLED | GreenLED
WaitingforTakeoff | 1 | 0 | X | 0 | 1
WaitingforTimer | 0 | 0 | X | 0 | 1
RaisingGear | X | 1 | 0 | 1 | 0
GearUp | X | 0 | X | 0 | 0
LoweringGear | X | 1 | 1 | 1 | 0
GearDown | X | 0 | X | 0 | 1
Gear Down
~PilotLever
GearIsDown
PilotLever

## Slide 65: Example Vending Machine
Taken from Katz & Borriello, “Contemporary Logic Design”

## Slide 66: Example: vending machine
Vending Machine FSM
N
D
Reset
Clock
Open
Coin Sensor
Release Mechanism
Release item after 15 cents are deposited
Single coin slot for dimes, nickels
No change

## Slide 67: Example: vending machine
Suitable abstract representation
  tabulate typical input sequences:
    3 nickels
    nickel, dime
    dime, nickel
    two dimes
  draw state diagram:
    inputs: N, D, reset
    output: open chute
  assumptions:
    assume N and D asserted for one cycle
    each state has a self loop for N = D = 0 (no coin)
S0
Reset
S2
D
S6
[open]
D
S4
[open]
D
S1
N
S3
N
S5
[open]
N
S8
[open]
D
S7
[open]
N

## Slide 68: Example: vending machine
Minimize number of states - reuse states whenever possible
symbolic state table
present inputs next output state D N state open 0¢ 0 0 0¢ 0 0 1 5¢ 0 1 0 10¢ 0 1 1 – – 5¢ 0 0 5¢ 0 0 1 10¢ 0 1 0 15¢ 0 1 1 – – 10¢ 0 0 10¢ 0 0 1 15¢ 0 1 0 15¢ 0 1 1 – – 15¢ – – 15¢ 1
0¢
Reset
5¢
N
N
N + D
10¢
D
15¢
[open]
D

## Slide 69: Example: vending machine
present state inputs next state output Q1 Q0 D N D1 D0 open 0 0 0 0 0 0 0 0 1 0 1 0 1 0 1 0 0 1 1 – – – 0 1 0 0 0 1 0 0 1 1 0 0 1 0 1 1 0 1 1 – – – 1 0 0 0 1 0 0 0 1 1 1 0 1 0 1 1 0 1 1 – – – 1 1 – – 1 1 1
Uniquely encode states

## Slide 70: Example: Moore implementation
D1 = Q1 + D + Q0 N
D0 = Q0’ N + Q0 N’ + Q1 N + Q1 D
OPEN = Q1 Q0
Mapping to logic
0 0 1 1
0 1 1 1
X X 1 X
1 1 1 1
Q1
D1
Q0
N
D
0 1 1 0
1 0 1 1
X X 1 X
0 1 1 1
Q1
D0
Q0
N
D
0 0 1 0
0 0 1 0
X X 1 X
0 0 1 0
Q1
Open
Q0
N
D

## Slide 71: Example: vending machine
present state inputs next state output Q3 Q2 Q1 Q0 D N D3 D2 D1 D0 open 0 0 0 1 0 0 0 0 0 1 0 0 1 0 0 1 0 0 1 0 0 1 0 0 0 1 1 - - - - - 0 0 1 0 0 0 0 0 1 0 0 0 1 0 1 0 0 0 1 0 1 0 0 0 0 1 1 - - - - - 0 1 0 0 0 0 0 1 0 0 0 0 1 1 0 0 0 0 1 0 1 0 0 0 0 1 1 - - - - - 1 0 0 0 - - 1 0 0 0 1
D0 = Q0 D’ N’
D1 = Q0 N + Q1 D’ N’
D2 = Q0 D + Q1 N + Q2 D’ N’
D3 = Q1 D + Q2 D + Q2 N + Q3
OPEN = Q3
One-hot encoding

## Slide 72: Mealy and Moore state diagrams
Moore machine
  outputs associated with state
0¢
[0]
10¢
[0]
5¢
[0]
15¢
[1]
N’ D’ + Reset
D
D
N
N+D
N
N’ D’
Reset’
N’ D’
N’ D’
Reset
0¢
10¢
5¢
15¢
(N’ D’ + Reset)/0
D/0
D/1
N/0
N+D/1
N/0
N’ D’/0
Reset’/1
N’ D’/0
N’ D’/0
Reset/0
Mealy machine
  outputs associated with transitions

## Slide 73: Example: Mealy implementation
0¢
10¢
5¢
15¢
Reset/0
D/0
D/1
N/0
N+D/1
N/0
N’ D’/0
Reset’/1
N’ D’/0
N’ D’/0
Reset/0
present state inputs next state output Q1 Q0 D N D1 D0 open 0 0 0 0 0 0 0 0 1 0 1 0 1 0 1 0 0 1 1 – – – 0 1 0 0 0 1 0 0 1 1 0 0 1 0 1 1 1 1 1 – – – 1 0 0 0 1 0 0 0 1 1 1 1 1 0 1 1 1 1 1 – – – 1 1 – – 1 1 1
D0 = Q0’N + Q0N’ + Q1N + Q1D
D1 = Q1 + D + Q0N
OPEN = Q1Q0 + Q1N + Q1D + Q0D
0 0 1 0
0 0 1 1
X X 1 X
0 1 1 1
Q1
Open
Q0
N
D

## Slide 74: Example: Mealy implementation
D0 = Q0’N + Q0N’ + Q1N + Q1D
D1 = Q1 + D + Q0N
OPEN = Q1Q0 + Q1N + Q1D + Q0D make sure OPEN is 0 when reset – by adding AND gate

## Slide 75: Moore to synchronous Mealy
OPEN = Q1Q0 creates a combinational delay after Q1 and Q0 change in Moore implementation
This can be corrected by retiming, i.e., move flip-flops and logic through each other to improve delay
OPEN.d = (Q1 + D + Q0N)(Q0'N + Q0N' + Q1N + Q1D) = Q1Q0N' + Q1N + Q1D + Q0'ND + Q0N'D
Implementation now looks like a synchronous Mealy machine
  it is common for programmable devices to have FF at end of logic

## Slide 76: Mealy to synchronous Mealy
OPEN.d = Q1Q0 + Q1N + Q1D + Q0D
OPEN.d = (Q1 + D + Q0N)(Q0'N + Q0N' + Q1N + Q1D) = Q1Q0N' + Q1N + Q1D + Q0'ND + Q0N'D
0 0 1 0
0 0 1 1
1 0 1 1
0 1 1 1
Q1
Open.d
Q0
N
D
0 0 1 0
0 0 1 1
X X 1 X
0 1 1 1
Q1
Open.d
Q0
N
D

## Slide 77: Types of FSMs
state feedback
inputs
outputs
reg
combinational logic for next state
logic for outputs
inputs
outputs
state feedback
reg
combinational logic for next state
logic for outputs
inputs
outputs
state feedback
reg
combinational logic for next state
logic for outputs
Moore
Mealy
Synchronous Mealy

## Slide 78: Sources
Prof. Mark G. Faust
John Wakerly