## Slide 1: Lecture 2
Topics
  Binary Arithmetic (Unsigned binary operands)
  Signed number representations
    Signed Magnitude
    Diminished Radix Complement (Ones Complement)
    Radix Complement (Twos Complement)
  Binary Arithmetic Revisited and Overflow
  Sign Extension

## Slide 2: Binary Arithmetic
Rules for “carry” same as in decimal
0
0
0
+
0
1
1
+
1
0
1
+
1
1
10
+
1
carry
Here are the rules for adding of each bit
carry

## Slide 3: Unsigned Binary (UB) Addition
Examples (4-bit word)
1011
0110
+
1
1
1
10001
0010
0110
+
1
1
1000
Overflow
2 + 6
2
+ 6
8
11
+ 6
17
11 + 6
17 > 24-1

## Slide 4: Overflow (Underflow)
10101101
01101100
Definition:
Result of an arithmetic operation is too large (or small) to be represented in number of bits available
Detection:
Varies with the representation. For unsigned binary, it’s determined by a carry out of the MSB
+
1
1
1
1
1
100011001
8 bit operands

## Slide 5: Signed Numbers
Have been assuming non-negative numbers
  Unsigned Binary (UB)
Several representations for signed numbers
  Sign Magnitude (SM)
  Diminished Radix Complement (DRC)
    1s Complement
  Radix Complement (RC)
    2s Complement

## Slide 6: Sign Magnitude
MSB functions as sign bit
0 = positive
1 = negative
Range of numbers:
-(2n-1 – 1) to +(2n-1 – 1)
n = 6
Two representations for 0
Negative formed by complementing sign bit
1510 = 001111SM
-1510 = 101111SM
010100SM = 2010
110100SM = -2010

## Slide 7: Diminished Radix Complement (DRC)
Called “Ones Complement”
MSB indicates sign
0 = positive
1 = negative
(but not a sign bit!)
Range of numbers:
-(2n-1 – 1) to +(2n-1 – 1)
Two representations for 0
Negative formed by complementing entire word
(called “taking the ones complement”)
  1510 = 001111DRC
  -1510 = 110000DRC
  010100DRC = 2010
  101011DRC = -2010

## Slide 8: Radix Complement (RC)
Called “Twos Complement”
MSB indicates sign
0 = positive
1 = negative
(but not a sign bit)
Range of numbers:
-(2n-1) to +(2n-1 – 1)
Only one representation for 0
Negative formed by complementing entire word
and adding 1 (called “taking the twos complement”)
  1510 = 001111RC
  -1510 = 110001RC
  010100RC = 2010
  101100RC = -2010

## Slide 9: Twos Complement – Special Cases
Notes: Note: Discard carry out of sign bit position!

## Slide 10: Twos Complement – Special Cases
Example: Take Twos Complement (RC)
of 0000 (010)
0000
1111
+ 1
0000
Complement
Add One
1
1
1
Ignore carry out of MSB
Note: Discard carry out of sign bit position!
Only one representation for 0

## Slide 11: Twos Complement – Special Cases
Example: Take Twos Complement (RC)
of 1000 (-810) (most negative)
1000
0111
+ 1
1000
Complement
Add One
1
1
1
Can’t represent
Complement of the most negative number
1000 (-810) is the most negative number
-810
+810 is not represented
Notes: Note: Discard carry out of sign bit position!

## Slide 12: Conversions of Signed Representations
From decimal
  Represent the absolute value of the number in UB
  Use the correct number of bits (add leading 0s)
  If the decimal number is negative, use the appropriate rule to negate the representation
    S/M – complement the sign bit
    DRC (ones complement) – complement every bit
    RC (twos complement) – complement every bit, add 1
To decimal
  If number is +, convert from UB to decimal (done!)
  If number is - use appropriate rule to negate it (obtain its absolute value)
    S/M – complement the sign bit
    DRC (ones complement) – complement every bit
    RC (twos complement) – complement every bit, add 1
  Convert this (positive) number as though UB to decimal
  Add a negative sign
Unsigned Binary
Sign Magnitude

## Slide 13: Why do we use RC (Twos Complement)?
BCD (which we’ll see shortly) was used in very early 4-bit microprocessors, but 2s complement is universally used now
Only one representation for zero
Simplified Addition
  Sign Magnitude Addition
    Must consider two operands without sign bits
    If sign bits same: perform add, check overflow
    If sign bits different: subtract (two cases)
      +A and – B  A – B
      – A and + B B – A
    Generate correct sign bit for sum
  Radix Complement (Twos Complement) Addition
    Just add!
Simple Subtraction
  Done via addition
    A + B
    A – B = A + (-B)
    Caution: Can’t take negative of most negative number

## Slide 14: Binary Arithmetic
Unsigned Binary (UB)
Signed Binary (SB)
Diminished Radix Complement (DRC)
  1s complement
Radix Complement (RC)
  2s complement
Rarely used

## Slide 15: Radix Complement (RC) or Twos Complement Addition
Examples (4-bit word)
0101
1001
+
1
1110
Ignore carry out of MSB
7 + (-2)
5 + (-7)
7
+ (-2)
5
5
+ (-7)
(-2)
0111
1110
+
1
1
10101
1

## Slide 16: Radix Complement (RC) or Twos Complement Addition
Examples (4-bit word)
Ignore carry out of MSB
-7 + (-2)
-7
+ (-2)
-9
1001
1110
+
10111
1
-9 < - (23)
We added two negative numbers and got a positive result!
Overflow!!

## Slide 17: Carry and Overflow

## Slide 18: Carry and Overflow
Is this an overflow condition?
If this is an unsigned binary (UB) number – Yes!
10101101
01101100
+
1
1
1
1
1
100011001
0
0
0

## Slide 19: Carry and Overflow
Is this an overflow condition?
If this is a radix complement (RC) number – No!
10101101
01101100
+
1
1
1
1
1
100011001
0
0
0
A negative number plus a positive number cannot produce an overflow

## Slide 20: Carry and Overflow Radix Complement (2s Complement)
Consider:
  Positive + Negative  Never overflow
  Negative + Negative  Overflow possible
  Positive + Positive  Overflow possible
Detecting Overflow:
  If signs of addends are same and sign of sum is different
  Equivalent to CSBP ¹ CSBP+1
C – Carry
SBP – Sign Bit Position

## Slide 21: Carry and Overflow
10101101
01101100
+
1
1
1
1
1
100011001
CSBP+1
CSBP
C – Carry
SBP – Sign Bit Position
0
0
0
CSBP = CSBP+1

## Slide 22: Radix Complement (RC) Addition
Examples (4-bit word)
1001
1110
+
10111
-7 + (-2)
-7
+ (-2)
-9
1
-9 < - (23)
We added two negative numbers and got a positive result!
0
0
0
CSBP+1
CSBP
CSBP+1 ¹ CSBP
Overflow!
Conclusion on Overflow in 2s Complement:
  There is an overflow if signs of addends are same and sign of sum is different
  Equivalent to CSBP ¹ CSBP+1
Notes: Returning to our previous example…

## Slide 23: Sign Extension
What happens when you move a number from a smaller word size to a larger one?
00000011
0000000000000011
(3)
(3)
11111101
0000000011111101
(253)
(253)
UB
00000011
0000000000000011
(3)
(3)
11111101
1000000001111101
(-125)
(-125)
S/M
00000011
0000000000000011
(3)
(3)
11111101
0000000011111101
(-3)
(+253!)
RC (2s complement)
11111101
1111111111111101
(-3)
(-3)
“extend” the sign bit left through the new MSB
Unsigned Binary is no problem, fill with zeros
Sign Magnitude is no problem, sign goes to MSB
23
bad
good

## Slide 24: Radix Complement (RC)
Called “Twos Complement”
MSB indicates sign
0 = positive
1 = negative
(but not a sign bit)
Range of numbers:
-(2n-1) to +(2n-1 – 1)
Only one representation for 0
Negative formed by complementing entire word
and adding 1 (called “taking the twos complement”)
  1510 = 001111RC
  -1510 = 110001RC
  010100RC = 2010
  101100RC = -2010
1 1 1 1 0 1
-3

## Slide 25: Sources
Prof. Mark G. Faust