## Slide 1: Lecture 3
Topics
  IEEE 754 Floating Point
  Binary Codes
    BCD
    ASCII, Unicode
    Gray Code
    7-Segment Code
    M-out-of-n codes
  Serial line codes

## Slide 2: Floating Point

## Slide 3: Floating Point
Need to represent “real” numbers
Fixed point too restrictive for precision and range
Not unlike familiar “scientific notation”
+ 6.022 x 1023
Sign
Mantissa
Exponent
Normalized mantissa – single digit to left of decimal point

## Slide 4: IEEE 754 Floating Point Standard
+ 1.101011 x 212
Sign
Mantissa
Exponent
Binary
A normalized (binary) mantissa will always have a leading 1
so we can assume it and get an extra bit of precision instead
Sign
Exponent
Significand
Fraction
1
Exponents are stored with a bias which is added to the exponent before being stored (allows fast magnitude compare)
Universally used on virtually all computers
Several levels of precision/range: Single, Double, Double-Extended

## Slide 5: IEEE 754 Floating Point Standard
Single Precision – 32 bits, Bias = 127
31
30
23
22
0
±
Exponent + Bias
Significand
1
8
23
F = -1Sign x (1+Significand) x 2(Exponent-Bias)

## Slide 6: IEEE 754 Floating Point Standard
Example
31
30
23
22
0
1
10000001
01000000000000000000000
1
8
23
F = -1Sign x (1+Significand) x 2(Exponent-Bias)
-
129
= 0.2510
= - 1.012 x 2(129-127)
= - 1.25 x 2(129-127)
= - 1.25 x 22
= - 1.25 x 4
= - 5.0
= - 1.012 x 2(129-127)
= - 1.012 x 22
= - 1012
= - 5.0

## Slide 7: IEEE 754 Floating Point Standard
Will commonly see these expressed as hex
31
30
23
22
0
1
10000001
01000000000000000000000
1
8
23
C0A00000
1010 A
1011 B
1100 C
8+4
8+2

## Slide 8: IEEE 754 Floating Point Standard
Some Special Cases
  Zero (no assumed leading 1)
    Exponent = 0, Significand = 0
  NaN (Not a Number), e.g. ¥
    Exponent = 255
  Denormalized (Subnormal) numbers
    Exponent = 0, Significand ¹ 0
F = -1Sign x (1+Significand) x 2(Exponent-Bias)
Bias = 127
Notes: IEEE 754-2008 now calls them subnormal

## Slide 9: IEEE 754 Floating Point Standard: subnormal numbers
Why do we need subnormal numbers?
    Addresses gap caused by implicit leading 1
    Smallest positive number (a) is 1.000…000 x 2-126
    Next number (b) is 1.000…001 x 2-126 = (2-126 + 2-149)
b
a
0
+
-
Gaps!
0 00000000 00000000000000000000000
0 00000000 00000000000000000000001
0 00000000 00000000000000000000010
0 00000000 00000000000000000000011
0 00000000 00000000000000000000100
= 0
= 1.00000000000000000000001 x 2-127
= 1.00000000000000000000010 x 2-127
= 1.00000000000000000000011 x 2-127
= 1.00000000000000000000100 x 2-127
S Exponent Significand
1 8 23
Distance from zero to smallest positive number is 1.00000000000000000000001 x 2-127 ~= 2-127
Distance to next number is 0.00000000000000000000001 x 2-127 = 2-23 x 2-127 = 2-150
  Subnormal numbers
    Exponent = 0, Significand ¹ 0

## Slide 10: IEEE 754 Floating Point Standard
Subnormal Numbers - properties
    Solution – Non-normalized form
    Exponent = 0, Significand ¹ 0
    Implicit Exponent of -126
    F = -1Sign x (Significand) x 2(-126)
    Smallest positive number (a) = 0.000…001 x 2-126 = 2-149
    Next smallest number (b) = 0.000…010 x 2-126 = 2-148

## Slide 11: Other IEEE 754 Formats
Half precision (binary16)
Single precision (binary32)
Double precision (binary64)
Quadruple precision (binary128)

## Slide 12: Other Formats: bias calculated from number of bits in the exponent
X86 Extended precision (80 bits)
Bias
Used in 8087 Math co-processor and subsequently in all x86 hardware floating point (intermediate operations).
Note explicit J-bit
2(5-1) – 1 = 24 -1 = 15
How to calculate the bias?

## Slide 13: BCD (Binary Coded Decimal)
Used in early 4-bit mP
Simple displays
4 Bits/Decimal Digit
2
5

## Slide 14: ASCII

## Slide 15: ASCII
American Standard Code for Information Interchange (pronounced: As’ key)
For encoding text
Universally used
  EBCDIC (old IBM mainframe standard) died
  Unicode for international (non-Roman) languages
    UTF-8 8-bit variable width encoding (1-4 bytes)
    UTF-16 16-bit variable width encoding
    UTF-32 32-bit fixed width encoding
UTF-8 commonly used for HTML/web browsers, FreeBSD, Linux
Gcc uses UTF-32

## Slide 16
“ECE171”
1000101100001110001010110001011011101100010000000
As a string of characters
E C E 1 7 1

## Slide 18: Gray Code

## Slide 19: Reflective Gray Code (RGC)
Adjacent codes differ by single bit
  “Unit Distance Code”
Often used in interfacing mechanical sensors
Shaft position

## Slide 20: Reflective Gray Code

## Slide 21: Reflective Gray Code (Conversion)
Notes: Explain modulo 2 (XOR) addition

## Slide 22: Reflective Gray Code (Conversion)
Notes: Explain modulo 2 (XOR) addition

## Slide 23: 7-Segment Code

## Slide 24: 1-out-of-n codes (1-hot)
8 devices
23 = 8
therefore 3 bits (wires) suffice…
if devoted 8 wires…
used in SCSI disk drives, PCI enumeration
000
001
111
With binary coded device selection
With 1-hot code coded device selection

## Slide 25: Serial Data Transmission & Storage

## Slide 26: Serial Data Transmission & Storage
Parallel
  Storage: each bit of word read/written simultaneously
  Transmission: each bit has separate signal path
Serial
  Reduce costs
  Simplify design
  Higher speed (LVDS, skew)
Applications
  USB
  PCI Express
Low Voltage Differential Signaling

## Slide 27: Serial Data Transmission & Storage
Clock
  Determines rate at which bits are transmitted (“bit rate”)
  “bit time”= clock period (1/bit rate) = “bit cell”
Sync
  Determines start of byte (or packet)
Data Format
  Determined by “line code”

## Slide 28: Codes for Serial Data Transmission and Storage
NRZ – Non Return to Zero
NRZI – Non Return to Zero Invert (on ones)
  Transition based
  Differential signaling: USB
RZ – Return to Zero
BPRZ – Bipolar Return to Zero
  “DC balanced”
  MLT-3 (100 Base T Ethernet)
Manchester encoding
  Guarantees a transition in every bit cell
  Facilitates clock recovery
  Requires higher bandwidth
  Original coax-based 10 Mbps Ethernet
Other techniques for DC balancing (and edge density)
  m-out-of-n-codes (e.g. 8B10B): Gigbabit Ethernet
Explain NRZI  transition based code (disk drives store don’t store 0s/1s but adjacent places may have different/same flux as neighbor, LVDS applications)
May need/want to explain source synchronous vs. embedded clocks and clock recovery
Notes: Explain NRZI  transition based code (disk drives store don’t store 0s/1s but adjacent places may have different/same flux as neighbor, LVDS applications)
May need/want to explain source synchronous vs. embedded clocks and clock recovery

## Slide 29: Why Serial?
Device A
Device B
10 bidirectional wires at 250Mbps
pair unidirectional wires at 2500Mbps (2.5Gbps)
“Parallel”
“Serial”
Device A
Device B
+
-
+
-

## Slide 30: Traditional Parallel Bus
Device A
Device B
Used in low to medium 100 MHz range
Issues
  Board trace length effect on skew
  Clock skew across devices
  Faster data rate squeezes “eye”
Because clock is distributed to both sender and receiver, its arrival time at sender and receiver is not simulataneous, and there will be skew with respect to the sent or received data.
Does everyone know what’s meant by “eye” – it’s the window during which data is expected to be valid. “Guardband” is test term which refers to the necessary “safety”, closing the eye. This is an issue in system performance, error rates, and of course in testing.

## Slide 31: Source Synchronous Bus
Device A
Device B
Used in 200MHz to 1.6GHz range
Clock signal is “forwarded” with data
Design impact:
  Board layout track length mismatch still adds to skew
  Eliminates skew error term caused by clock domain skew
  Allows faster cycle times than parallel

## Slide 32: Embedded Clock
Clock signal is “embedded” with data
  Received used digital phase locked loop (DPLL) to “recover” clock and determine where bit times are
  Edge density must guaranteed by encoding scheme
Examples
  PCI Express, USB, Serial RapidIO, Infiniband
  Intel’s new QuickPath Interconnect
Data
Clock
Clock signal embedded with data
We’ll look at the encoding scheme which ensures this in a moment

## Slide 33: Edge Lock Technique (Tracking Receiver)
Device
A
Device A sends pulse train to Device B
Device B “locks” onto edges to be in sync with pulse stream
Device
B
In order to achieve locking and clock recovery we need to ensure a certain density of edge transitions – this is where the encoding scheme comes in…

## Slide 34: Ensuring Edge Density: m-of-n codes
Some 8-bit code words have too few 1s (or 0s) to ensure edge density sufficient to recover clock
8b10 encoding (developed by IBM in 1983)
  Use 10-bit code words, but only use a subset of the available 210 code words
    No more than five 0s or 1s in a row
    Balanced number of 0s and 1s (difference between count of 0s and 1s in a string of at least 20 bits is no more than two.
  Benefits
    Ensure edge density
    Avoid DC bias at receiver from imbalance
      Running disparity for unbalanced codewords
  256 data characters
    All 8-bit bytes
    12 control characters (INIT, etc)
8 bit byte
10 bit code
Table lookup
TX FIFO
8B/10B Encoder
Serializer
RX FIFO
8B/10B Decoder
Deserializer
Parallel Data
RX FIFO
8B/10B Decoder
Deserializer
Parallel Data
TX FIFO
8B/10B Encoder
Serializer
Parallel Data
Parallel Data
+
_
+
_
Device A
Device B

## Slide 35: Error Detection and Correction
Errors occur during data storage/retrieval and transmission
  Noise, cross-talk, EMI, cosmic rays, impurities in IC materials
  More common with high speeds, lower voltages
Use m-out-of-n codes to detect errors
  Not all possible codes are used (valid)
  Errors in used (valid) codes (hopefully) produce unused (invalid) codes
Notes: Parity, ECC, CRC

## Slide 36: Example of Error Detection and Correction
Example: Luhn Algorithm
  Credit cards, IMEI (International Mobile Equipment Identity)
    Start from right, double every second digit
    Add all digits
    Add a final check digit to ensure sum is multiple of 10
Notes: Parity, ECC, CRC

## Slide 37: Differential Signaling
Differential, point to point
  Complementary signals transmitted
  Receiver detects voltage difference between lines
  Low amplitudes (200mV - 400mV typical), high speeds
  Good noise immunity
    Pair routed together – noise cancels out
LVDS – Low Voltage Differential Signaling
  ANSI/TIA/EIA 644-1995 standard (signaling only, not protocol or connectors)
  3.125 Gbps, +/- 350mV
  “Gbps at mWs” -- High speed & low power consumption
  FibreChannel, Gigabit Ethernet, HDMI, DVI, USB
Well suited to NRZI encoding – only care about transitions – signals “cross”
ANSI – American National Standards Institute
TIA Telecommunications Industry Association
EIA Electronics Industries Alliance
Edge rather than level sensitive!!!!
LVDS is a common technique and used in DVI and HDMI (Digital Video I/F) and (High Definition Multimedia I/F)

## Slide 38: Differential Signaling

## Slide 39: Sources
Prof. Mark G. Faust
John Wakerly