## Slide 1: Lecture 9
Topics
  Glitches and Hazards
    Hazard Types (Function, Logic), (Static, Dynamic)
    Recognizing Static Logic Hazards
    Correcting Static Logic Hazards
  Types of Functions and Delays
    Trivial, Simple, 1- and 2- and Multilevel Gate Circuits
  Decoders and Multiplexers

## Slide 2: Glitches and Hazards
Notes: Note: even gates on the same IC will not have exactly identical propagation delays and then of course there are different “wire”/trace path lengths.

## Slide 3: Glitches and Hazards
Glitch: Momentary error condition on the output of a circuit due to unequal signal delay paths. Manifestation of a hazard.
Function Hazard: May cause glitch when two or more inputs change at once. Cannot be removed by adding logic.
Logic Hazard: May cause glitch when one input changes. Can be removed by adding logic.
Dynamic Hazard: Occurs when output of the circuit is changing.
Static Hazard: Occurs when output of the circuit is constant.
Function and Logic Hazards can be Static or Dynamic.
Note: even gates on the same IC will not have exactly identical propagation delays and then of course there are different “wire”/trace path lengths.

## Slide 4: Static Logic Hazards
Single input changed.
Resulting output should have remained the same:
  1 in case(a), 0 in case(b).
However, a glitch appeared before the output settled back to its correct level.
In two-level SOP circuits may see static 1 hazards
In two-level POS circuits may see static 0 hazards

## Slide 5: Static Logic Hazards
Consider inputs
ABC
111
110
0
1
1
1
1
0
1
0
NAND/NAND Implementation
1
1
0

## Slide 6: Static Logic Hazards
Consider inputs
ABC
111
110
0
1
1
1
1
0
1
0
NAND/NAND Implementation
1
1
0
Let’s look in detail at how a static logic hazard might arise, how it would manifest itself as a glitch and what you can do about it.
Mention simulation
Also mention that the glitch may not make a difference – synchronous design which you’ll learn later (for now, just know that we may only “look” at the output after a certain “settling” time.

## Slide 7: Detecting and Eliminating Static Logic Hazards
Chain Link Rule

## Slide 8: Detecting and Eliminating Static Logic Hazards

## Slide 9: Another Example
Implement a hazard-free circuit for the 0s of the previous function using NOR gates
SOP Form for 0s
Need Cover Term

## Slide 10: Static Function Hazards
Result of two or more input signals changing
Cannot be removed by adding logic

## Slide 11: Dynamic Hazards
Generally occur in multi-level circuits when there are multiples paths with different delays from an input to an output.
Do not occur in 2-level SOP (or POS) implementations.

## Slide 12: Implementations for Complex Functions and Their Delays

## Slide 13: Decoders

## Slide 14: Decoders
n-to-2n decoder
Converts binary code on input lines to one of 2n output lines
When a decoder has an EN (enable) input it’s often called a demultiplexer (dmux). EN is often active low.
I1
I0
Y0
Y1
Y2
Y3
I1
I0
Y0
Y1
Y2
Y3
EN
I1
I0
EN
Y0
Y1
Y2
Y3

## Slide 15: Decoders
B1B0 F0F1F2F3
0 0 0 1 1 1
0 1 1 0 1 1
1 0 1 1 0 1
1 1 1 1 1 0
Sometimes outputs are active low too!

## Slide 16: Decoders as Universal Function Implementers
Outputs are minterms
I1
I0
Y0 (m0)
Y1 (m1)
Y2 (m2)
Y3 (m3)
Any function can be expressed in canonical SOP form

## Slide 17: Decoders
When using decoders with active low outputs use “bubble matching” to use correct gate
Example: Implement XNOR with DMUX

## Slide 18: Multiplexers

## Slide 19: Multiplexers (Data Selectors) Mux
Directs one of 2n inputs to a single output
S0D1D0 F
0 0 0 0
0 0 1 1
0 1 0 0
0 1 1 1
1 0 0 0
1 0 1 0
1 1 0 1
1 1 1 1
S0 F
0 D0
1 D1

## Slide 20: Multiplexers
Sometimes include Enable input
EN S0 F
0 0 D0
0 1 D1
1 X 0
Effective as universal function generator
Just as decoders were effective as minterm generators (simple functions) and could be used in combination with an OR (NAND) gate to generate functions, a Mux can be used to generate complex functoin

## Slide 21: Type 0 Universal Function Implementation with a Mux
Uses the function inputs (X,Y,Z) to “select” the value of the function by selecting the minterm corresponding to the inputs. If the minterm mi is in the function the corresponding Di input is tied to 1 (0 otherwise)

## Slide 22: Type 1 Universal Function Implementation with a Mux

## Slide 23: A word about “optimization”
What are we optimizing?
  Variables (inputs – connectors)
  Terms (gates, interconnect)
  Unique fan-in (IC packages – same number of gates)
  Number of logic levels (speed)
  NAND/NOR Implementations (speed, IC packages,…)
  Complexity (Design time – time to market)
  Design Time & Flexibility/Cost (FPGA vs. ASIC)

## Slide 24: Sources
Prof. Mark G. Faust
John Wakerly