## Slide 1: Theory of Event Expressions
Tool to design motions directly from symbols.
This theory is general enough to allow arbitrary motion to be symbolically described but is also detailed enough to allow the designer or the robot to precise the generated behavior to the most fundamental details.
Our main concept is that the motion is a sequence of symbols, each symbol corresponding to an elementary action such as shaking head for answering “yes”.
We will call them primitive motions.
The complex motions are created by combining primitive motions.

## Slide 2
What are the factors of motion that are important to generation of symbolic motions, especially in dance and pantomime?
The research issues are:
  (1) What should be the primitive, basic or atomic motions?
  (2) What should be the operations on motions that combine primitive motions to complex motions?
  (3) How symbolic motions are reflected/realized as physical motions of real robots?
  (4) How to create existing and new symbolic motions automatically using some kind of knowledge-based algebraic software editor.

## Slide 3
Human-robot emotion-augmented communication systems.
The new extended communication media in addition to:
  speech
  will include prosody
  facial gestures
  hand gestures
  body language
    head and neck,
    legs,
    bending of full body,
    muscle-only motions
  The gestures used in daily communication,
  ritual gestures of all kinds,
  theatric and
  dance motions
will be captured or translated to certain algebraic notations.

## Slide 4
the same grammar.
The unified notations will allow also to transform between various media.
For instance, a captured motion of a flower can be presented as motion of a pantomime actor.
A sound pattern can be transformed to a pattern of colored laser lights.
Sound, light, theatric stage movements, special effects and robot motions have all the same nature of sequences of symbolic event-related atoms.
Thus the theater itself becomes a super-robot with the ability to express its emotional state through various motions, lights and theater plays orchestration.
These sequences can be uniformly processed.
We propose to create universal editors that will be not specialized to any particular medium or robot.
They will use algebraic and logic based notations.

## Slide 5: on-line versus off-line creation of motions
Film is an art that does not require feedback from the audience and every presented event is always exactly the same.
  Creation has been done earlier, off-line with the director and his associates as the audience during shooting and editing.
In contrast, the theatre performance is always slightly different and it depends on the feedback from the audience.
The public may say “Actor X had a good day today”.
The research questions are:
  (1) “will the future robot theatre be more similar to films or theatrical performances?”,
  (2) “can one create a realistic robot theatre without viewer’s feedback?”
  (3) “What type of tools do we need to create a theater play off-line versus on-line?”,
  (4) “Is an off-line sequence generator enough to create art?”
  (5) “Do we need a sequence generator and a virtual reality simulator before actuate the play on the robot”?
  (6) “How really important is the feedback from the audience for a human singer or conference speaker to modify their on-stage behaviors? a

## Slide 6
How it should be reflected in the on-line robot theatre?
Should we have a “character” of each robot simulated together with the performance?
  (So that a shy robot should run from the stage if it is booed.
  A strong robot should remain.
  But maybe the shy robot will know much better how to express the meaning of the play.)
In general, do we need a “character” to use the feedback from audience or should be this simulated otherwise?”

## Slide 7: Event Expressions to specify languages of motions and behaviors
A regular expression is a pattern that matches one or more strings of characters from a finite alphabet.
Individual characters are considered regular expressions that match themselves.
Original regular expressions used union, concatenation and iteration operators.
Regular expressions were next extended by adding negation and intersection to a Boolean Algebra.
Observe that X1 ∩ X2 is an empty set for atoms X1  X2 , as the meaning of intersection operator is set-theoretical.
Similarly the interpretation of  operator is set-theoretical in regular expressions, thus new symbols are not being created.

## Slide 8
Greeting_1 = (Wave_Hand_Up o Wave_Hand_Down ) (Wave_Hand_Up o Wave_Hand_Down ) *  Wave_Hand_Up o Say_Hello
Which means, to greet a person the robot should execute one of two actions:
  Action 1: wave hand up, follow it by waving hand down. Execute it at least once.
  Action 2: Wave hand up, next say “Hello”. The same is true for any complex events.
As we see, the semantics of regular expressions is used here, with atomic symbols from the terminal alphabet of basic events {Wave_Hand_Down, Wave_Hand_Up , Say_Hello}.
The operators used here are: concatenation (o), union () and iteration (*). Each operator has one or two arguments.
So far, these expressions are the same as regular expressions.
Initial state
Final state
Wave_Hand_Up
Say_Hello
Wave_Hand_Up
Wave_Hand_Down

Wave_Hand_Up
Wave_Hand_Down

## Slide 9
They are now expanded to event expressions by recursively adding more deterministic and probabilistic operators on event expressions
For instance, if we agree that the meaning of every operator in Greeting_1 is that it executes its first argument with probability ½ and its second argument with the same probability, each possible sequence from the infinite set of motions of Greeting_1 will have certain probability of occurrence.
One can create event expressions using both deterministic and probabilistic, single-argument and two-argument operators.
Extending to Event Expressions

## Slide 10: Event Expressions to specify languages of motions and behaviors
The base ideas of event expressions are these:
  (1) Symbol (represented by sequence of characters) is a basic event or a set of basic events synchronized and executed in parallel.
  (2) Symbols can be connected in parallel (for instance, (a) text spoken, (b) leg motion, and (c) hand motion can be created relatively independently and combined in parallel). Connecting symbols in parallel creates new symbols that can be used as macros

## Slide 11
For instance, assuming that concatenation is a deterministic operator and union is a probabilistic operator with equal probabilities of both arguments, there is a probability of ½ that the robot will greet with motion Wave_Hand_Up o Say_Hello .
Assuming that all operators are probabilistic operators with equal probabilities of both arguments, for event expression Wave_Hand_Up o Say_Hello there is a probability of ½ that the robot will greet with one of the following four motions, each with the same probability:
  (1) Wave_Hand_Up o Say_Hello ,
  (2) Wave_Hand_Up ,
  (3) Say_Hello ,
  (4) Nothing will happen.

## Slide 12
As we see, in this case for each of two arguments of concatenation there is the probability of ½ that it happens and probability of ½ that it does not happen.
Similarly, the user of the editor can use many operators, deterministic or probabilistic to define event expressions.
Several such operators are created for any standard operator of regular expression.
Next, the user can define his/her own new operators.
These operators can have temporal, multiple-valued and probabilistic/deterministic nature.
Our system of Event Expressions and corresponding state machines uses an expanded set of operators taken from multiple-valued logic; literals, MAX, MIN, truncated-sum, Modulo-addition and others.
The symbols are interpreted as having numerical values for them.
This allows also for interpolation (Hermite, Spline, Radial Basis) and spectral operators based on Fast Fourier Transform (FFT).
Extending to Event Expressions

## Slide 13: Brzozowski’s derivatives
All words of E, starting from letter Xj є X. If the letter is removed from the front of each word from the set, a new language is created, referred to as left-side-derivative of language E by letter Xj.
This new language is now denoted by E/Xj.
A derivative for word s = Xi1, Xi2…Xin is defined as follows:
  E/Xj = {s є X* : Xjs є E}.
As inherent laws of Brzozowski’s derivative method, the following properties Pi always hold true.

## Slide 14: Recursive Rules for PMG design
P1. Xi/Xj = e for i = j
= ø for i ≠ j
P2. (E1 ∪ E2)/Xi = E1/Xi ∪ ∈ E2/Xi
P3. ∈(E) = e when e ∈ E
= ø when e ∉ E
P4. E1E2/Xi=(E1/Xi)E2∪∈ (E1)(E2/Xi)
P5. E/s=E1/Xi1Xi2…Xin=[[E/Xi1]/Xi2]…]/Xin
P6. E*/Xi = (E/Xi)E*
P7. E/e = E
P8. (E1 ∩ E2)/Xi = (E1/Xi) ∩ (E2/Xi)
P9. (-E)/Xi = -(E/Xi)
P10. (E1 max E2)/Xi = (E1/Xi) max (E2/Xi)
In our system there are many other rules similar to rule P10 for MIN, MAX and other MV operators.
There are many rules similar to P9 for literals and rules similar to P8, P2, P6 and P4 for probabilistic variants of operators ∩,∪, and concatenation, respectively

## Slide 15: Example of designing PMG from Event Expression
Language is given E1 = (X2X1* ∪ X1X2).
Applying the left-side-derivative with respect to first character in string, X1
  E1/X1 = (X2X1* ∪ X1X2)/X1
  = (X2X1*)/X1 ∪ (X1X2)/X1
  by P2
  = (X2/X1)X1* ∪ ∈ (X2)X1* ∪ (X1/X1)/X2 ∪ ∈ (X1)(X2/X1)
  by P4
  = ø X1 ∪ ø(X1/X2) ∪ eX2 ∪ ø ø
  by P1
  = X2

## Slide 16
Fig. 2. Graph for regular language
E1 = (X2X1* ∪ X1X2).
It can be interpreted as PMG, EEAM or BM depending on meaning of symbols Xi

## Slide 17: Acceptor, generator and transformer
Observe that this graph can be interpreted as an acceptor, when symbols Xi are inputs.
It can be interpreted as a generator when symbols Xi are outputs.
The graph can be thus used to recognize if some motion belongs to some language and can generate a motion belonging to the language.
This graph is realized in software

## Slide 18
Input text
Output text
Hexapod walking
Distance evaluation
Biped walking
Number of falls
evaluation
Biped Gestures
Comparison to video evaluation
Hand gestures
Subjective human evaluation
Learning problems in Human-Robot Interaction – Motion Behavior (input/output) generation problems
Behavior Problems = examples of correct motions – generalize and modify, interpolate