## Slide 1: Gray-Scale Morphology

## Slide 2: Z2 and Z3
set in mathematic morphology represent objects in an image
  binary image (0 = white, 1 = black) : the element of the set is the coordinates (x,y) of pixel belong to the object  Z2
gray-scaled image : the element of the set is the coordinates (x,y) of pixel belong to the object and the gray levels  Z3

## Slide 3: Extension from Binary Morphology to Gray-Scale Morphology
deal with digital image function
  f(x,y) : the input image
  b(x,y) : a structuring element (a subimage function)
assumption : these functions are discrete
  (x,y) are integers
  f and b are functions that assign a gray-level value (real number or real integer) to each distinct pair of coordinate (x,y)

## Slide 4: Gray Scale Morphology
In this morphology, the binary dilation, erosion, opening, closing are naturally extended to gray scale
extension: uses min or max operation
  gray scale dilation: surface of dilation of umbra
  gray scale dilation: maximum and a set of addition operations
  gray scale erosion: minimum and a set of subtraction operations

## Slide 5: Gray Scale Dilation and Erosion: the concepts of TOP and UMBRA
top: top surface of A: denoted by
umbra of f: denoted by

## Slide 6: A function f and its Umbra U[f]
top surface of A:
Umbra are all points that are smaller or equal than the top surface

## Slide 7: Gray-Scale Dilation

## Slide 8: Gray-Scale Dilation with Max and shift
Df and Db are the domains of f and b, respectively
dilation
Shifts in both directions

## Slide 9: Gray-Scale Dilation
Simple function f
Structuring Element b of height A
Result of dilation of various positions of sliding b past f
Complete result of dilation shown in solid

## Slide 10: Gray-Scale Dilation
Df and Db are the domains of f and b, respectively
condition that (s-x) and (t-y) have to be in the domain of f and (x,y) have to be in the domain of b is similar to the condition in binary morphological dilation where the two sets have to overlap by at least one element

## Slide 11: Gray-Scale Dilation Characteristics
Gray Scale Dilation is similar to 2D convolution
  f(s-x) : f(-x) is simply f(x) mirrored with respect to the original of the x axis. the function f(s-x) moves to the right for positive s, and to the left for negative s.
  max operation replaces the sums of convolution
  addition operation replaces with the products of convolution
general effect of Gray Scale Dilation
  if all the values of the structuring element are positive, the output image tends to be brighter than the input
  dark details either are reduced or eliminated, depending on how their values and shapes relate to the structuring element used for dilation

## Slide 12: Gray Scale Dilation Using Umbra
gray scale dilation: surface of dilation of umbras
dilation of f by k: denoted by

## Slide 13
Gray Scale Dilation Using Umbra
Dilating the umbras of f and k
Finding the top surface T
umbra of k

## Slide 14: Gray Scale Dilation with Umbra

## Slide 15
Calculations of Gray Scale Dilation Using Umbra
We want to calculate f dilation by K

## Slide 16
Representation of K

## Slide 17
Representation of F

## Slide 18: Calculations of Gray Scale Dilation

## Slide 21
F dilation by k
Representation of F dilation by k

## Slide 22: Gray Scale Erosion

## Slide 23: Gray Scale Erosion
condition (s+x) and (t+y) have to be in the domain of f and (x,y) have to be in the domain of b is similar to the condition in binary morphological erosion where the structuring element has to be completely contained by the set being eroded
erosion

## Slide 24: Gray Scale Erosion
similar to 2D correlation
  f(s+x) moves to the left for positive s and to the right for negative s.
general effect
  if all the elements of the structuring element are positive, the output image tends to be darker than the input
  the effect of bright details in the input image that are smaller in area than the structuring element is reduced, with the degree of reduction being determined by the gray-level values surrounding the bright detail and by the shape and amplitude values of the structuring element itself

## Slide 25: Dual property of Gray-scale Erosion and Dilation
gray-scale dilation and erosion are duals with respect to function complementation and reflection.

## Slide 26: Example: Gray Scale Dilation and Erosion
result of dilation with a flat-top structuring element in the shape of parallelepiped of unit height and size 5x5 pixels
note: brighter image and small, dark details are reduced
result of erosion
note: darker image and small, dark details are reduced

## Slide 27: Gray Scale Erosion with Umbra
gray scale erosion: surface of binary erosions of one umbra by the other umbra

## Slide 28: Original Lena Image
=lena.im=
Dilation of Lena

## Slide 29: Dilated Lena Image
=lena.im.dil=

## Slide 30
Structuring Elements:
Value=0
 | * | * | * | 
* | * | * | * | *
* | * | * | * | *
* | * | * | * | *
 | * | * | * | 

## Slide 31: Gray Scale Erosion with Umbra

## Slide 32: Gray Scale Erosion with Umbra

## Slide 33: Gray Scale Dilation Erosion (cont’)

## Slide 34: Gray Scale Dilation and Erosion (cont’)

## Slide 35: Gray Scale Dilation and Erosion (cont’)

## Slide 36: Calculations for a Gray Erosion

## Slide 37: Gray Scale Erosion (cont’)

## Slide 38: Gray Scale Erosion of Lena
=lena.im.ero=

## Slide 39: Gray Scale Dilation and Erosion (cont’)
erosion
dilation
original

## Slide 40: Gray Scale Dilation and Erosion (cont’)
Perspective projection surface plot forms

## Slide 41: Umbra Homomorphism Theorems
surface and umbra operations: inverses of each other, in a certain sense
surface operation: left inverse of umbra operation
For dilation and for erosion

## Slide 42: Umbra Homomorphism Theorems
Proposition 5.1
Proposition 5.2
Proposition 5.3

## Slide 43: Gray Scale Opening and Closing

## Slide 44: Gray Scale Opening and Closing
gray scale opening of f by kernel k denoted by f k
gray scale closing of f by kernel k denoted by f k
opening
closing

## Slide 45: Gray Scale Opening of Lena
=lena.im.open=

## Slide 46: Gray Scale Closing of Lena
=lena.im.close=

## Slide 47: Duality of Gray Scale Opening and Closing
duality of gray scale, dilation erosion duality of opening, closing
ORIGINAL IMAGE
Sharpened IMAGE
g

## Slide 48
h

## Slide 49: Openings, Closings and Medians
median filter: most common nonlinear noise-smoothing filter
  median filter: for each pixel, the new value is the median of a window
  median filter: robust to outlier pixel values leaves, edges sharp
median root images: images remain unchanged after median filter

## Slide 50: Discuss hardware design of median filter and sorting

## Slide 51: Gray Scale Opening

## Slide 52: Opening and closing gray-level images
a gray-scale scan line
positions of rolling ball for opening
result of opening
positions of rolling ball for closing
result of closing
view an image function f(x,y) in 3D perspective, with the x- and y-axes and the gray-level value axis

## Slide 53: Properties of Opening and Closing for Gray Level Images
dual property
opening operation satisfies
closing operation satisfies
note:
er indicates that the domain of e is a subset of the domain of r, and also that e(x,y) ≤ r(x,y) for any (x,y) in the domain of e

## Slide 54: Effects of opening
  the structuring element is rolled underside the surface of f
  all the peaks that are narrow with respect to the diameter of the structuring element will be reduced in amplitude and sharpness
  so, opening is used to remove small light details,
    while leaving the overall gray levels and larger bright features relatively undisturbed.
  the initial erosion removes the details, but it also darkens the image.
  the subsequent dilation again increases the overall intensity of the image without reintroducing the details totally removed by erosion

## Slide 55
EFFECTS of OPENING: Example of Gray-Scale Opening
  the structuring element is rolled underside the surface of f
  all the peaks that are narrow with respect to the diameter of the structuring element will be reduced in amplitude and sharpness
  so, opening is used to remove small light details,
    while leaving the overall gray levels and larger bright features relatively undisturbed.
  the initial erosion removes the details, but it also darkens the image.
  the subsequent dilation again increases the overall intensity of the image without reintroducing the details totally removed by erosion

## Slide 56: Gray Scale Closing

## Slide 57: Effect of closing

## Slide 58: EFFECTS of CLOSING: Example of Gray-Scale Closing
  the structuring element is rolled on top of the surface of f
  peaks essentially are left in their original form (assume that their separation at the narrowest points exceeds the diameter of the structuring element)
  so, closing is used to remove small dark details, while leaving bright features relatively undisturbed.
  the initial dilation removes the dark details and brightens the image
  the subsequent erosion darkens the image without reintroducing the details totally removed by dilation

## Slide 59: Some Applications of Gray-scale Morphology
Morphological smoothing
Morphological gradient
Top-hat transformation
Textural segmentation
Granulometry
Note: the examples shown in this topic are of size 512x512 and processed by using the structuring element in the shape of parallelepiped of unit height and size 5x5 pixels

## Slide 60: Gray Scale Morphological smoothing

## Slide 61: Morphological smoothing
perform an opening following by a closing
effect: remove or attenuate both bright and dark artifacts or noise

## Slide 62: Morphological gradient
effect: gradient highlight sharp gray-level transitions in the input image.

## Slide 63: Top-hat transformation
effect: enhancing detail in the presence of shading
note: the enhancement of detail in the background region below the lower part of the horse’s head.

## Slide 64: Textural segmentation

## Slide 65: Textural segmentation
the region the right consists of circular blobs of larger diameter than those on the left.
the objective is to find the boundary between the two regions based on their textural content.

## Slide 66: Textural segmentation
Original image
Image showing boundary between regions of different texture

## Slide 67: Textural segmentation
Perform
  closing the image by using successively larger structuring elements than small blobs
    as closing tends to remove dark details from an image, thus the small blobs are removed from the image, leaving only a light background on the left and larger blobs on the right
  opening with a structuring element that is large in relation to the separation between the large blobs
    opening removes the light patches between the blobs, leaving dark region on the right consisting of the large dark blobs and now equally dark patches between these blobs.
  by now, we have a light region on the left and a dark region on the right, so we can use a simple threshold to yield the boundary between the two textural regions.
white | black

## Slide 68: Gray Scale Granulometry

## Slide 69: What is Granulometry?
determining the size distribution of particles in an image.
from the example, the image consists of light objects of 3 different sizes
the objects are not only overlapping but also cluttered to enable detection of individual particles

## Slide 70: Granulometry
Original image for granulometry
Size distribution of granules in the image
Overlapping granules
objects are lighter than background

## Slide 71: Procedure of Granulometry
Perform
  opening with structuring elements of increasing size on the original image
  the difference between the original image and its opening is computed after each pass when a different structuring element is completed
  at the end of the process, these differences are normalized and then used to construct a histogram of particle-size distribution
idea: opening operations of a particular size have the most effect on regions of the input image that contain particles of similar size.

## Slide 73: Sources
傅楸善 & 王林農
r94922081@ntu.edu.tw
Morris