## Slide 1: ECE590 HW1, VHDL SORTER
JAN FURE

## Slide 2: DESIGN GOAL
Create sorter that sorts 3 numbers at a time for the purpose of speeding up the sorting process.
Hypothesis is that if sorter alternates between 3 at a time, and 2 at a time sorting entities, the average number can get transported 1.5 positions per clock cycle.

## Slide 3: HIGH LEVEL IMPLEMENTATION
Behavioral description consisting of a single entity.
Input and output are length N * W STANDARD_LOGIC_VECTOR, where N is how many numbers to sort, and W is the word length in bits of the numbers.
N can be any positive integer greater than 2.

## Slide 4: FIRST IMPLEMENTATION
Every other sort step sorts 3 and 2 numbers respectively.
Detects numbers as sorted when the output of each sort state is the same.
Restricted to sorting multiples of 3 numbers, i.e. 3,6,9 etc.

## Slide 5: Second Implementation
Uses 3 sort states.
Each sort state uses an array of units that sort 3 numbers, staggered relative to each the other sort states.
The ends have “padding” of flip flops, allowing sorting of arbitrary number of elements.
Has a preferential direction of transport.
Detects if numbers are sorted in 2 clock cycles.

## Slide 6: PERFORMANCE
Sort Architecture | Sort3/Sort2 | Sort3/Sort3/Sort3
Random 12 bytes #1 | 12 | 13
Random 12 bytes #2 | 10 | 13
Move 1 byte (of 12) to right | 10 | 10
Move 1 byte (of 12) to left | 10 | 13
Move all bytes | 15 | 14
Move 1 byte (of 30) to right | 22 | 19
Move 1 byte (of 30) to left |  | 31