## Slide 1: Review
We presented several examples of simple fuzzy controllers
Now we will present more advanced controllers.

## Slide 2
Fuzzy logic representation of Uncertainty using Production Rules

## Slide 3: Production Rules
Assuming that the knowledge-base module contains knowledge represented in the format of production rules the following sections introduce the following:
    the concept of a production rule
    the concept of linguistic variables
    the fuzzy inference concept
    the concept of fuzzification and how to accomplish the crisp to fuzzy transformation
    the concept of defuzzification and how to accomplish the fuzzy to crisp transformation

## Slide 4: Knowledge presentation using production rules
From a philosophical point the concept of knowledge is highly ambiguous and debatable
Knowledge-base builders treat knowledge from a narrower point of view: utilitarian, rules, facts, etc.
This way the knowledge is easier to model and understand.
It remains diverse including:
  rules,
  facts,
  truths,
  reasons,
  defaults and
  heuristics.
The knowledge engineer needs some technique for capturing what is known about the application.

## Slide 5: Various types of Knowledge representation using production rules
The production rules technique should provide expressive adequacy and notational efficacy.
Knowledge representation is very much under constant research.
Several schemes have been suggested in the literature, namely:
  semantic nets,
  frames and
  logic.
Production rules have also been suggested and are the most popular way of representing knowledge.

## Slide 6: Knowledge presentation using production rules
Production rules are small chunks of knowledge expressed in the form of if..then statements.
  The left hand side (IF) represents the antecedent or conditional part.
  The right hand side (THEN) represents the conclusion or action part.
  A number of rules collectively define a modularized know-how system.
  The principal use of production rules is in the encoding of empirical associations between incoming patterns of data and actions that the system should perform as a consequence.
  The production rules are either expressed by an expert of the field, or derived using induction.

## Slide 7
Fuzzy logic Control

## Slide 8: Fuzzy Logic Control
Fuzzy controller design consist of turning intuitions, and any other information about how to control a system, into set of rules.
  These rules can then be applied to the system.
If the rules adequately control the system, the design work is done.
If the rules are inadequate, the way they fail provides information to change the rules.
Analyze experimentally, change

## Slide 9: Example: Control a Plant
A valve in an internal combustion engine that regulates the amount of vaporized fuel entering the cylindres

## Slide 10: FLAKEY ROBOT = Fuzzy Logic for Autonomous Vehicle Motion Planning
EXAMPLE 1

## Slide 11: Using Fuzzy Logic for Autonomous Vehicle Motion Planning
Findings of Stanford Research Institute (SRI)
Based on the performance of the robot “Flakey” circa 1993
Discussion of autonomous navigation and path planning in an uncertain environment
Paper: “Using Fuzzy Logic for Autonomous Vehicle Motion Planning”

## Slide 12: Difficulties of a classical robot control problem
Autonomous operation of a mobile robot in a real-world unstructured environment poses a series of problems:
  knowledge about the environment is usually:
    incomplete
    uncertain, and
    approximate
  Perceptually acquired information is not reliable:
    noise introduces uncertainty and imprecision
    limited range and visibility introduces incompleteness
    errors in interpretation

## Slide 13: More Difficulties with classical robot Problem
Real world environments have complex and largely unpredictable dynamics
  objects can move
  the environment may be modified
  features may change
– Vehicle action execution is not reliable:
    the results produced by sending a given command to an effector can only be approximately estimated
    action execution may fail entirely

## Slide 14: Robot Architecture using Fuzzy Controller
Key is “Local
Perceptual
Space”:
LPS is a data structure
providing
geometric
picture around
vehicle
Camera,etc
Map of the rooms
LPS
Flakey
Local Perceptual Space (LPS)
Goals are represented in the LPS by means of control structures

## Slide 15: The Fuzzy Controller
Physical motion of the robot is based on a complex fuzzy controller
  The controller provides a layer of robust high-level motor skills.
Basic building block of controller is a “behavior”:
    A behavior is defined as implementing an atomic motor skill aimed at achieving or maintaining a give goal situation
      – e.g. follow a wall.
Flakey

## Slide 16: Implementing Behaviors
Each behavioral skill is represented by means of a “desirability function” that expresses preferences over possible actions with reference to the goal:
  e.g. a behavior aimed at following a given wall prefers actions that keep the agent parallel to the wall at a safe distance
Flakey
desirability function

## Slide 17: Behavior through Fuzzy Rules
Each behavior was implemented by a set of fuzzy rules of the form
  IF A THEN C
    A is composed of fuzzy predicates and connectives, and
    C is a fuzzy set of control vectors
  An example of a “keep off” behavior rule is:
IF obstacle-close-in-front AND NOT obstacle-close-on-left THEN turn-sharp-left
Flakey

## Slide 18: Fast Reactive Behaviors
Purely reactive behaviors, intended to provide quick simple reactions to potential dangers typically use sensor data
  This sensor data has undergone little or no interpretation.
Since quick response is necessary to avoid disaster, little processing can be done.
Flakey
Rules can be implemented in an FPGA

## Slide 19: Control Structures
Purposeful behavior like attempting to reach a certain location must take explicit goals into consideration.
Goals are represented in the LPS by means of control structures.
Control structure is a triple
  S = (A,B,C)
    A is a virtual object (artifact) in the LPS
    B is a behavior that specifies the way to react to the presence of this object, and
    C is a fuzzy predicate expressing the context where the control structure is relevant
Flakey

## Slide 20: Control Structure Example
An example control structure is
  S1=(CP1, go-to-CP, near(CP1)
    CP1 is a control-point (marker for a location), together with a heading and a velocity
    go-to-CP reacts to the presence of S1 in the LPS by generating the commands to reach the location, heading and velocity specified by CP1.
go-to-CP includes rules like:
  IF facing(CP1) AND too-slow-for(CP1) THEN accelerate-smooth-positive
  S = (A,B,C)
    A is a virtual object (artifact) in the LPS
    B is a behavior that specifies the way to react to the presence of this object, and
    C is a fuzzy predicate expressing the context where the control structure is relevant
Flakey

## Slide 21: Blending of Behaviors
Many behaviors can be simultaneously active
Fuzzy controller selects the controls that best satisfy the active behaviors
Satisfaction is weighted by each behavior’s relevance to the current situation.
  e.g. can’t follow a wall if there isn’t one
Context dependent blending of behaviors is implemented by combining the output of all the behaviors using context rules
Flakey

## Slide 22: Generating a plan:
simple goal-regressing planner used:
  based on a topological map annotated with approximate measurements (no obstacles) working backwards from goal.
An example plan might be:
S1 = (Obstacle, keep-off, near(Obstacle))
S2 = (Corr1, follow,~near(obstacle) AND at(Corr2) AND
~near(Corr2))
S3 = (Corr2, follow,~near(obstacle) AND at(Corr2) AND
~near(Door5))
S4 = (Door5, cross,~near(Obstacle) AND near(Door5))
Control structure
Flakey
  S = (A,B,C)
    A is a virtual object (artifact) in the LPS
    B is a behavior that specifies the way to react to the presence of this object, and
    C is a fuzzy predicate expressing the context where the control structure is relevant

## Slide 23: Executing the Plan
Flakey
S1 = (Obstacle, keep-off, near(Obstacle))
S2 = (Corr1, follow,~near(obstacle) AND at(Corr2) AND
~near(Corr2))
S3 = (Corr2, follow,~near(obstacle) AND at(Corr2) AND
~near(Door5))
S4 = (Door5, cross,~near(Obstacle) AND near(Door5))

## Slide 24: Cruise Control Example of Fuzzy Logic Controller
EXAMPLE 2

## Slide 25: Example design of a Fuzzy Logic Control System – Cruise Control
  The block diagram of the intelligent cruise control system.

## Slide 26: Input membership functions for Cruise Control
The three input membership functions
Shows fuzzification of three inputs
Membership values in Y axis
Car’s Speed Relative to Cruise Setting Membership Function
Difference in Car’s Speed Relative to Cruise Setting
Car’s Speed in Miles per Hour
Car’s Speed Membership Functions
Space Distance in Feet
Distance from Car Ahead

## Slide 27: Fuzzy Logic Rules Table for Cruise Control
cruise speed | slow / distance from car ahead |  |  |  |  | fast / distance from car ahead |  |  |  | 
 | 15 | 30 | 45 | 60 | 75 | 15 | 30 | 45 | 60 | 75
+10 | 0.15 | 0.15 | 0.15 | 0.15 | 0.15 | 0.15 | 0.15 | 0.15 | 0.15 | 0.15
+5 | 0.15 | 0.15 | 0.35 | 0.35 | 0.35 | 0.15 | 0.15 | 0.15 | 0.35 | 0.35
0 | 0.15 | 0.50 | 0.50 | 0.50 | 0.50 | 0.15 | 0.15 | 0.35 | 0.50 | 0.50
-5 | 0.35 | 0.65 | 0.65 | 0.85 | 0.85 | 0.15 | 0.35 | 0.50 | 0.65 | 0.85
-10 | 0.35 | 0.65 | 0.85 | 0.85 | 0.85 | 0.15 | 0.50 | 0.65 | 0.85 | 0.85
All combinations in this particular case are specified using a 3-Dimensional Table.
For more dimensions you can use Kmap or Marquand Chart.

## Slide 28: Output membership function for Cruise Control
The output is the accelerator percentage change needed to keep the car a safe distance behind the car ahead and to keep the car at cruising speed.
Membership values in X axis
From fuzzy to crisp

## Slide 29: Fuzzy Inference: creating fuzzy output

## Slide 30: Fuzzy Inference: creating fuzzy output
At the end of the fuzzification step the working memory module contains the values of the fuzzified input.
  Each production rule is examined and all the rules that have their premises satisfied `fire'.
  Hence, the only rules which do not fire are those that at least one of their premises has a membership degree of zero.
  In the case that more than one rule fires, this is common and desirable, the system generates a single fuzzy output.
    This is achieved by combining all fuzzy outputs.
  The single fuzzy output is then passed to the defuzzification module which generates a crisp value.
    Then the system is ready to start the entire process all over again.

## Slide 31: SIMPLE EXAMPLE: a four-rule system
EXAMPLE 3

## Slide 32: SIMPLE EXAMPLE: a four-rule system
Assumptions
  Let X,Y and Z be the linguistic variables.
  X and Y are inputs , Z is output.
  Let the membership functions be low and high.
  Let the membership functions be the same for all linguistic variables.
  Define the membership functions as:
    low(linguistic) = 1 - t
    high(linguistic) = t
      where t is a value in the interval [0,1].

## Slide 33: A Simple Example (Membership Functions)
LOW
HIGH
Memberships functions in both X and Y axes

## Slide 34: A Simple Example (Rules)
The rule base contains the following four rules:
  if X is low and Y is low then Z is high (rule-1)
  if X is low and Y is high then Z is low (rule-2)
  if X is high and Y is low then Z is low (rule-3)
  If X is high and Y is high then Z is high (rule-4)
X
Y
LOW
HIGH
LOW
HIGH
  Z is high (rule-1)
  Z is low (rule-2)
  Z is low (rule-3)
  Z is high (rule-4)
Aggregate Rules
Defuzzify

## Slide 35
Aggregation is the process of unification of the outputs of all rules. We take the membership functions of all rule consequents previously clipped or scaled and combine them into a single fuzzy set.
The input of the aggregation process is the list of clipped or scaled consequent membership functions, and the output is one fuzzy set for each output variable.
Aggregation of the rule outputs

## Slide 36: A Simple Example (Calculations)
Next assume that the inputs are 0 and 0.32 for the linguistic variables X and Y respectively.
  The problem then is to find if Z is high or low and its crisp value.
The next steps are followed:
  Step-1: Find the membership grade for the premises of each rule. We have 8 premises but due to replication only 4 are needed.
    Low(X) = 1- t = 1-0 = 1
    Low(Y) = 1- t = 1-0.32 = 0.68
    High(X) = t = 0
    High(Y) = t = 0.32
This is our decision
X=0
Y= 0.32

## Slide 37: A Simple Example (Rules)
The rule base contains the following four rules:
  if X is low and Y is low then Z is high (rule-1)
  if X is low and Y is high then Z is low (rule-2)
  if X is high and Y is low then Z is low (rule-3)
  If X is high and Y is high then Z is high (rule-4)
X
Y
LOW
HIGH
LOW
HIGH
  Z is high (rule-1)
  Z is low (rule-2)
  Z is low (rule-3)
  Z is high (rule-4)
Aggregate Rules
Defuzzify
X=0
Y= 0.32
1
X=0
0.68
0.68
1
0.32

## Slide 38: A Simple Example (Calculations)
  Step-2: Identify the rules that can fire. In our case only the first two rules can fire since the last two rules have a premise with a zero degree of membership.
  Step-3: For each rule that can fire find the strength of the firing.
    Rule-1 = min(1,0.68) = 0.68
    Rule-2 = min(1,0.32) = 0.32
    Note that min is used because the premises are connected with a logical AND.

## Slide 39: A Simple Example (Calculations)
  Step-4: All the fuzzy outputs are combined together to form a single fuzzy subset.
  One way is to take the pointwise maximum value over all fuzzy outputs.
    In our case we have two fuzzy outputs, so for each point we take the maximum value.

## Slide 40: A Simple Example (Calculations)
  Step-5: The fuzzy combined output needs to be converted to a single crisp value.
  Using one method which takes the Average-of-Maxima.
    With this method one finds the maximum peak of the fuzzy combined output - in our case this is 0.68.
  Then one collects all the t values for which the maximum value occurs - in our case there are 42 cases.
  Finally, the crisp value is the average of such variables - in our case 0.84.

## Slide 41: Development Cycle for simple fuzzy cotroller
Do not discuss in the class – this is home reading

## Slide 42: Development Cycle

## Slide 43: Development Cycle
  Step 1: The goal is to establish the characteristics of the system, and also to define the specific operating properties of the proposed fuzzy model.
    Traditional systems analysis and knowledge engineering techniques can be employed at this stage. The designer must identify the relevant and appropriate inputs to the system; the basic transformations, if any, that are performed on the inputs,; and what output is expected from the system.
    The designer must also decide if the fuzzy system is a subsystem of a `global' system and if so to define where the fuzzy subsystem fits into the `global architecture', or if it is the `global' system itself.
    The numerical ranges of inputs and outputs must also be specified. This step applies to the development of all systems. Be prepared to throw away original versions at this stage.

## Slide 44: Development Cycle
  Step 2: The goal is to decompose each control variable (i.e., inputs and outputs) into fuzzy sets and to give unique names to them.
    It has been reported in the literature that the number of labels associated with a control variable should generally be odd and between five and nine.
    Also, in order to obtain a smooth transition from a state to another each label should overlap somewhat with its neighbours. Overlapping of 10 to 50 percent is advised.
    Finally, the density of the fuzzy sets should be highest around the optimal control point of the system and should thin out as the distance from that point increases.

## Slide 45: Development Cycle
If possible begin with an exhaustive list of production rules
Deal with redundant, impossible and implausible rules and/or conditions later.
  When the number of rules increases dramatically, may be several rule-bases might be constructed.
  Each rule-base to deal with a particular situation/condition of the system to be modelled.

## Slide 46: Development Cycle
  Step 3: The goal is to obtain the production rules that tie the input values to the output values.
  Since each production rule `declares' a small chunk of knowledge, the order in the knowledge base is unimportant.
  Nevertheless, in order to maintain the knowledge base one should group the production rules by their premise variable.
  How many rules is obviously dependent on the application and is related to the number of control variables.

## Slide 47: Development Cycle
  Step 4: The goal is to decide on the way that is going to be used in order to convert a an output fuzzy set into a crisp solution variable.
  There are many ways to perform the conversion but usually process control applications use the centroid technique.
  The rest of the steps are similar to any modelling exercise.
    For instance, at the end of the fuzzy system construction the process of simulation commences.
    The model is compared against known test cases and the results are validated.
    When the results are not as desired changes are made until the desired performance is achieved.

## Slide 48: Popular Fuzzy Inference Methods

## Slide 49: Popular Fuzzy Inference Methods
Under the fuzzy inference process the grade of each premise is found and applied to the conclusion part of each rule.
  MIN or PRODUCT are two popular inference methods.
  With MIN inferencing the output of the conclusion part is clipped off at a height equal to the rule's degree of firing.
    This was used in the simple example before and the MIN inference for the first rule is re-shown below
    (Recall that the rule's degree of firing was 0.68):

## Slide 50: MIN
0.68

## Slide 51: PRODUCT
With PRODUCT inferencing the output membership function is scaled by the rule's degree of firing.
Using the first rule of the simple example and the PRODUCT inference we get the following

## Slide 52: Product

## Slide 53: Popular methods for combining outputs

## Slide 54: Popular methods for combining outputs
Under the combining outputs process all outputs are combined together to produce a single fuzzy output.
  MAX and SUM are two popular techniques for combining outputs.
  With MAX the pointwise maximum for all fuzzy outputs is taken.
  For the first rule of the simple example we used the MAX techniques which resulted in the following diagram:

## Slide 55: Max

## Slide 56: SUM
With SUM the pointwise sum for all fuzzy outputs is taken.
Again for the first rule of the simple example we get:
Observe that we operate in fuzzy space, all inputs and outputs are in fuzzy interval [0, 1]

## Slide 57
The most commonly used fuzzy inference technique is the so-called Mamdani method.
In 1975, Professor Ebrahim Mamdani of London University built one of the first fuzzy systems to control a steam engine and boiler combination.
He applied a set of fuzzy rules supplied by experienced human operators.
Fuzzy inference:
Clipping versus Scaling

## Slide 58
Now the result of the antecedent evaluation can be applied to the membership function of the consequent.
The most common method of correlating the rule consequent with the truth value of the rule antecedent is to cut the consequent membership function at the level of the antecedent truth.
This method is called clipping.
Since the top of the membership function is sliced, the clipped fuzzy set loses some information.
However, clipping is still often preferred because it involves less complex and faster mathematics, and generates an aggregated output surface that is easier to defuzzify.

## Slide 59
While clipping is a frequently used method, scaling offers a better approach for preserving the original shape of the fuzzy set.
The original membership function of the rule consequent is adjusted by multiplying all its membership degrees by the truth value of the rule antecedent.
This method, which generally loses less information, can be very useful in fuzzy expert systems.

## Slide 60
Clipped and scaled membership functions
Degree of
Membership
Degree of
Membership
Clipped
Scaled

## Slide 61: Defuzzification

## Slide 62: Popular defuzzification methods
Under the defuzzification process a fuzzy output is converted to a crisp number.
  Two of the more popular techniques are the MAXIMUM and the CENTROID.
  With MAXIMUM one selects the maximum value of the fuzzy output as the crisp value.
  There are several variations to the MAXIMUM theme.
    One such variation is the AVERAGE-OF-MAXIMA which was used in the simple example and gave us a crisp value of 0.84.
With the CENTROID method, the center of gravity of the fuzzy output gives the crisp value.
Using PRODUCT inferencing and the SUM combination the CENTROID results in a crisp value of 0.56.

## Slide 63: Calculating the output of a rule

## Slide 64: Ways of Combining Fuzzy Logic Output Values
There are four different
techniques to combine the fuzzy logic rules output
values.
They are:
Maximizer
Average
Centroid
Singleton
Observe that we no longer operate here in fuzzy interval [0, 1]
Temperature not fuzzy value

## Slide 65
  With MAXIMUM one selects the maximum value of the fuzzy output as the crisp value.
With the CENTROID method, the center of gravity of the fuzzy output gives the crisp value.

## Slide 66: Another approach to Calculating the output of a rule
Rules have promises which are usually combined together by the connective and.
The output is calculated by taking the degree of membership of the lesser of all premises as the value of the combination and truncating the output fuzzy set at that level.

## Slide 67: Calculating the output of a rule (cont)
Truncated at 0.2
Rules have promises which are usually combined together by the connective and.
The output is calculated by taking the degree of membership of the lesser of all premises as the value of the combination and truncating the output fuzzy set at that level.

## Slide 68: Combining rule outputs
When all rules have been evaluated a single fuzzy set is calculated by combining all outputs.
The combination involves the connective or.
The single output is calculated by taking the maximum of their respective output fuzzy sets grades at each point along the horizontal axis.

## Slide 69: Combining rule outputs
Shifted horizontally
Think about the set of fuzzy rules as a network with fuzzy literals and operators MIN, MAX, etc. In primary inputs you have fuzzification, in primary outputs you have defuzzification. The network analogy is very useful in your thinking about fuzzy logic, mv logic, or any other kind of data structure to store knowledge.
Do in class a complete example of designing a fuzzy logic network for a simple robot control with about 6 rules. Discuss various operators and fuzzifiers, defuzzifiers.

## Slide 70
The most popular one is the centroid technique. It finds the point where a vertical line would slice the aggregate set into two equal masses.
Mathematically this centre of gravity (COG) can be expressed as:
x
x
dx
x
dx
Defuzzification
The input for the defuzzification process is the aggregate output fuzzy set and the output is a single number.

## Slide 71
Centroid defuzzification method finds a point representing the centre of gravity of the fuzzy set, A, on the interval, ab.
A reasonable estimate can be obtained by calculating it over a sample of points.

## Slide 72
Centre of gravity (COG):

## Slide 73: STATIC, ADAPTIVE, SELF-ORGANISING SYSTEMS

## Slide 74: STATIC, ADAPTIVE, SELF-ORGANISING SYSTEMS
Up to now we have seen that fuzzy logic supports the task of designing a control system.
  What we examined in previous sections is known as the `static' fuzzy system.
  In such a system, conventional techniques are employed in order to elicit or induce production rules.
  Such a system, receives inputs which are then normalised and converted to fuzzy representations, the knowledge base is executed, an output fuzzy set is generated which is then converted to a crisp value.

## Slide 75: “static” fuzzy system.

## Slide 76: ADAPTIVE, SELF-ORGANISING SYSTEMS
  The rules do not change, except if modified by the hand of the designer, for all the knowledge base lifetime.
  Static systems are fine for applications in which the environment is known and predictable.
    But because they can not adapt to gradual changes in their environments they can lead to disaster when the assumptions upon which they are built are violated.
An adaptive system adjusts to time or process conditions.
This means that such a system modifies:
  - the charactersitics of the rules,
  the topology of the fuzzy sets, and
  the method of defuzzification
  among others.

## Slide 77: An adaptive system

## Slide 78: ADAPTIVE, SELF-ORGANISING SYSTEMS
A performance metric, often another expert system or an algorithm, compares the current and the stored array of past solutions and the comparison result is passed to an adaptation machine..
The adaptation machine, often another expert system, decides what changes to make in the underlying fuzzy model.
  For instance:
    the contribution weights connected with each rule can be modified or
    the membership functions re-drawn.

## Slide 79: Questions and Problems (1)
Explain Linguistic Variables in Expert Systems.
Explain and illustrate these concepts: fuzzifying, fuzzy rule base, fuzzy inference, defuzzifying
Give various methods to explain the concept of uncertainty in robotics.
Uncertainty versus fuzziness.
Explain Fuzzy Control in robot Flakey.
What is LPS?
Blending of behaviors and generating a plan in Flakey. What is the advantage of fuzzy logic?
Compare, subsystem after subsystem, a fuzzy controller with a classical controller.
Cruise Control Example of Fuzzy Logic Controller, how can you improve it for more sensors, more motors and more advanced rules?
Give an example how to create a fuzzy rule table.
Read the Four-Rules example. Explain how to use graphics to calculate values of operators. Use this example to explain how a more complicated Braitenberg Vehicle would work. Assume that it has to execute both Aggressive and Shy behaviors and we use another sensor or combination of sensors to change from one to another behavior.

## Slide 80: Questions and Problems (2)
Explain stages of the development cycle using fuzzy logic for a simple Braitenberg-Vehicle like robot with more sensors than 5.
Explain graphical methods for MIN, MAX, SUM, PRODUCT and other operators.
Explain on example how these methods to calculate outputs work: Centroid, Maximum, Average-of-Maxima.
Explain and illustrate the concepts of Static, Versus Adaptive, versus Self-Organizing Fuzzy Systems.
Discuss the misconceptions about fuzzy logic: fuzzy logic is fuzzy thinking, fuzzy logic is probabilistic, fuzzy logic means no math, fuzziness is vague.
Explain Mamdani’s Controller for Cement Kiln. How to go from Operator’s Manual to Fuzzy Rules. How to select values of parameters?
Explain the Takagi-Sugeno Fuzzy Control System.
Give and explain five examples of Fuzzy Systems and invent a new fuzzy system by yourself.

## Slide 81: HOMEWORK 3 (different than fuzzy homework this year)
This homework should be returned by December 1.
Homework 3 should involve Fuzzy Logic control for a robot.
  Software should be written in LISP.
  You can use also ANN, kinematics, inverse kinematics, etc as part of your expert system.
This should be the robot from your project.
Robot should have some kind of sensors and some kind of effectors.
The robot should respond with its motions to the changes of the environment (mobile robot avoids obstacles, follow a line, follow a corridor, etc, robot arm puts blocks on top of one another, etc).
The control of the robot should use fuzzy logic.
Example of good robot arm is here
http://www.androidworld.com/prod61.htm

## Slide 82
http://www.mendeley.com/research/realistic-behaviour-simulation-humanoid-robot-5/

## Slide 83: Sources
    Paul and Mildred Burkey
    Saba Rahimi
    Weilin Pan
    Xuekun Kou
    A. Ferworn
    Kevin Morris
    Dr Dimitris Tsaptsinos
      Kingston University, Mathematics
      http://www.kingston.ac.uk/~ma_s435
      ma_s435@kingston.ac.uk